## Slide 1: Do-more Designer v2.3
New BRX I/O Hardware

## Slide 2: Current BRX I/O Offering
10 discrete IN
12 discrete OUT
5 discrete IN/OUT
2 analog IN
1 temperature IN
2 analog OUT
TOTAL: 32 modules

## Slide 3: Current BRX I/O Offering (10 Discrete IN)
10 discrete IN
Discrete Input Modules |  |  |  |  | 
Identifier | Type | 8-Point | 12-Point | 16-Point | 32-Point
NF3 | 3-5 VDC Sink/Source | BX-08NF3 | - | - | -
ND3 | 12-24 VDC Sink/Source | BX-08ND3 | BX-12ND3 | BX-16ND3 | BX-32ND3
NB | 24 VAC | BX-08NB | BX-12NB | BX-16NB | -
NA | 120 VAC | BX-08NA | BX-12NA | BX-16NA | -
SIM | Simulator | BX08SIM | - | - | -
11 discrete IN
12 discrete IN
New BRX I/O Offering (12 Discrete IN)

## Slide 4: Current BRX I/O Offering (12 Discrete OUT)
12 discrete OUT
Discrete Output Modules |  |  |  |  |  | 
Identifier | Type | 5-Point | 8-Point | 12-Point | 16-Point | 32-Point
TD1 | 12-24 VDC Sinking | - | BX-08TD1 | BX-12TD1 | BX-16TD1 | BX-32TD1
TD2 | 12-24 VDC Sourcing | - | BX-08TD2 | BX-12TD2 | BX-16TD2 | BX-32TD2
TR | Relay Form A (SPST) | - | BX-08TR | BX-12TR | BX-16TR | -
TRS | Relay Form C (SPDT) | BX-05TRS | - | - | - | -
TA | 120-240 VAC Triac | - | BX08TA | BX-12TA | - | -
14 discrete OUT
New BRX I/O Offering (14 Discrete OUT)

## Slide 5: New 32-Point Modules Require ZIPLink
32-Point BRX Discrete I/O ZIPLink Selector |  |  |  |  | 
Module | ZIPLink Module | ZIPLink Module P/N | Qty Needed | ZIPLink Cable P/N | Qty Needed
BX-32ND3 | Feedthrough | ZL-RTB40 ZL-RTD40-1 | 1 | ZL-D24-CBL40 ZL-D24-CBL40-1 ZL-D24-CBL40-2 | 1
BX-32TD1 |  |  |  |  | 
BX-32TD2 |  |  |  |  | 
A<>B switch for the LEDs

## Slide 6: Current BRX I/O Offering (2 Analog IN)
2 analog IN
5 analog IN
New BRX I/O Offering (5 Analog IN)
Analog Input Modules |  |  | 
Identifier | Type | Resolution | 8-Channel
AD-1 | Current Sink 0-20mA, 4-20mA | 16-bit | BX-08AD-1
AD-2B | Voltage ±10VDC, ±5VDC 0-5VDC, 0-10VDC | 16-bit | BX-08AD-2B
Analog Input Modules |  |  |  | 
Identifier | Type | Resolution | 4-Channel | 8-Channel
ADM-1 | Current Sink 0-20mA, 4-20mA | 14-bit | BX-04ADM-1 | -
AD-1 | Current Sink 0-20mA, 4-20mA | 16-bit | BX-04AD-1 | BX-08AD-1
AD-2B | Voltage ±10VDC, ±5VDC 0-5VDC, 0-10VDC | 16-bit | BX-04AD-2B | BX-08AD-2B

## Slide 7: Current BRX I/O Offering (1 Temperature IN)
1 temperature IN
4 temperature IN
New BRX I/O Offering (4 Temperature IN)
Temperature Input Modules |  | 
Identifier | Type | 4-Channel
THM | Thermocouple | BX-04THM
Temperature Input Modules |  |  |  | 
Identifier | Type | 4-Channel | 6-Channel | 8-Channel
THM | Thermocouple | BX-04THM | - | BX-08THM
RTD | Resistance Temperature Detector | - | BX-06RTD | -
NTC | Thermistor | - | - | BX-08NTC

## Slide 8: Current BRX I/O Offering (2 Analog OUT)
2 analog OUT
4 analog OUT
New BRX I/O Offering (4 Analog OUT)
Analog Output Modules |  |  | 
Identifier | Type | 8-Point | 4-Point
DA-1 | Current Source 0-20mA, 4-20mA | BX-08DA-1 | BX-04DA-1
DA-2B | Voltage ±10VDC, ±5VDC, 0-5VDC, 0-10VDC | BX-08DA-2B | BX-04DA-2B

## Slide 9: NEW BRX I/O Offering
12 discrete IN
14 discrete OUT
5 discrete IN/OUT
5 analog IN
4 temperature IN
4 analog OUT
TOTAL: 44 modules
No changes

## Slide 10: Do-more Designer v2.3
New BRX I/O Hardware Configuration

## Slide 11: New BRX I/O Modules
Discrete IN
BX
-
32ND3
No
BX
-
08SIM
No
NEW MODULE
Module Configuration
Discrete OUT
BX
-
32TD1
No
BX
-
32TD2
No
Analog IN
BX
-
04ADM
-
1
Yes
BX
-
04AD
-
1
Yes
BX
-
04AD
-
2B
Yes
Temperature IN
BX
-
08THM
Yes
BX
-
06RTD
Yes
BX
-
08NTC
Yes
Analog OUT
BX
-
04DA
-
1
Yes
BX
-
04DA
-
2B
Yes

## Slide 12: New BRX Analog IN Configuration
BX-04ADM-1 – current sink, 0-20mA, 4-20mA, 14-bit
  Global Settings
    Name
    Channels Enabled (1-4)
  Analog Inputs 1-4
    Analog Input
      0-20mA
      4-20mA
    Enable Scaling
      WX Min/Max (Counts, mA)
      RX Min/Max
      Clamp RX

## Slide 13: New BRX Analog IN Configuration
BX-04AD-1 – current sink, 0-20mA, 4-20mA, 16-bit
  Global Settings
    Name
    Channels Enabled (1-4)
  Analog Inputs 1-4
    Analog Input
      0-20mA
      4-20mA
      Enable 16-bit
    Enable Scaling
      WX Min/Max (Counts, mA)
      RX Min/Max
      Clamp RX
Enable 16-bit unipolar data:
- Default: 0 to +32,767 (current IN)
- 16-bit: 0 to +65,535 (must use WX0:U)

## Slide 14: New BRX Analog IN Configuration
BX-04AD-2B – voltage, ±10VDC, ±5VDC, 0-5VDC, 0-10VDC, 16-bit
  Global Settings
    Name
    Channels Enabled (1-4)
  Analog Inputs 1-4
    Analog Input
      0-5VDC
      0-10VDC
      ±5VDC
      ±10VDC
      Enable 16-bit
    Enable Scaling
      WX Min/Max (Counts, VDC)
      RX Min/Max
      Clamp RX
Enable 16-bit unipolar data:
- Default unipolar: 0 to +32,767
- 16-bit: 0 to +65,535 (must use WX0:U)
- Default bipolar: -32,768 to +32,767 (already 16-bit)

## Slide 15: New BRX I/O Modules
NEW MODULE
Module Configuration
Discrete IN
BX
-
32ND3
No
BX
-
08SIM
No
Discrete OUT
BX
-
32TD1
No
BX
-
32TD2
No
Analog IN
BX
-
04ADM
-
1
Yes
BX
-
04AD
-
1
Yes
BX
-
04AD
-
2B
Yes
Temperature IN
BX
-
08THM
Yes
BX
-
06RTD
Yes
BX
-
08NTC
Yes
Analog OUT
BX
-
04DA
-
1
Yes
BX
-
04DA
-
2B
Yes

## Slide 16: New BRX Temperature IN Configuration
BX-08THM – thermocouple
  Global Settings
    Name
    Channels Enabled (1-8)
    Temperature Scale (°F/°C)
    Burn Out Mode (Disabled / Low/High Side)
  Analog Inputs 1-4 / 5-8
    Analog Input
      J, K, E, R, S, T, B, N, C
      0-39mVDC, 0-156mVDC, 0-1.25VDC
      ±39mVDC, ±78mVDC, ±156mVDC
      Enable 16-bit
    Enable Scaling
      WX Min/Max (Counts, Deg)
      RX Min/Max
      Clamp RX
Burn Out Mode:
- Disabled: burn-out bit OFF, channel  0xFFFF
- Low side: burn-out bit ON, channel = 0
- High side: burn-out bit ON, channel = 0xFFFF

## Slide 17: New BRX Temperature IN Configuration
BX-06RTD – resistance thermal detector
  Global Settings
    Name
    Channels Enabled (1-6)
    Temperature Scale (°F/°C)
    Burn Out Mode (Disabled / Low/High Side)
    Channel Range (JPt100, Pt100, Pt1000, Cu10, Cu25, Ni20, 0-10K, 0-6.25K, 0-3.125K, 0-1.563K, 0-781.3, 0-390.6, 0-195.3)
    Conversion Rate/Accuracy
      16Hz / 16-bit / 125ms
      470Hz / 14-bit / 4ms
  Analog Inputs 1-4 / 5-6
    Enable Scaling
      WX Min/Max (Counts, Deg)
      RX Min/Max
      Clamp RX

## Slide 18: New BRX Temperature IN Configuration
BX-08NTC – thermistor
  Global Settings
    Name
    Channels Enabled (1-8)
    Temperature Scale (°F/°C)
    Burn Out Mode (Disabled / Low/High Side)
    Channel Range (1.8K, 2252, 3K, 5K, 10K-AN, 10K-CP)
    Conversion Rate/Accuracy
      16Hz / 16-bit / 125ms
      470Hz / 14-bit / 4ms
  Analog Inputs 1-4 / 5-8
    Enable Scaling
      WX Min/Max (Counts, Deg)
      RX Min/Max
      Clamp RX

## Slide 19: New BRX I/O Modules
NEW MODULE
Module Configuration
Discrete IN
BX
-
32ND3
No
BX
-
08SIM
No
Discrete OUT
BX
-
32TD1
No
BX
-
32TD2
No
Analog IN
BX
-
04ADM
-
1
Yes
BX
-
04AD
-
1
Yes
BX
-
04AD
-
2B
Yes
Temperature IN
BX
-
08THM
Yes
BX
-
06RTD
Yes
BX
-
08NTC
Yes
Analog OUT
BX
-
04DA
-
1
Yes
BX
-
04DA
-
2B
Yes

## Slide 20: New BRX Analog OUT Configuration
BX-04DA-1 – current source, 0-20mA, 4-20mA
  Global Settings
    Name
    Channels Enabled (1-4)
  Analog Outputs 1-4
    Analog Output
      0-20mA, 4-20mA
      Enable 16-bit
    Enable Scaling
      RY Min/Max
      WY Min/Max (Counts, mA)
      Clamp WY

## Slide 21: New BRX Analog OUT Configuration
BX-04DA-2B – voltage, 0-5VDC, 0-10VDC, ±5VDC, ±10VDC
  Global Settings
    Name
    Channels Enabled (1-4)
  Analog Outputs 1-4
    Analog Output
      0-5VDC, 0-10VDC, ±5VDC, ±10VDC
      Enable 16-bit
    Enable Scaling
      RY Min/Max
      WY Min/Max (Counts, VDC)
      Clamp WY

## Slide 22: Do-more Designer v2.3
New BRX Remote Bases

## Slide 23: New BRX Remote I/O Bases
BX
-
EBC100
-
M
BX
-
MBIO
-
M
BX
-
DMIO
-
M
Protocol
H2/T1H
-
EBC100
ERM/EBC
Yes
Modbus TCP
Yes
Modbus RTU
Ethernet I/O
Yes
Yes
Yes
Yes
Yes
Yes
Yes
Ethernet Base Controller
Modbus I/O
Do-more I/O
H2 | T1H
$329 | $287
AC | DC
$269 | 249
AC | DC
$254 | $234
AC | DC
$179 | $159

## Slide 24: New BRX Remote I/O Bases
EBC100
DMIO
MBIO
ERM protocol
Do-more
Ethernet I/O
Modbus
TCP
Modbus
RTU

## Slide 25: BX-DMIO
BRX Do-more I/O

## Slide 26: Configuration: BX-DMIO-M
2 models: 120-240 VAC or 12-24 VDC supply
8 expansion I/O modules
10/100 Mbps port
DIP Switches

## Slide 27: Configuration: BX-DMIO-M
IP configuration:
  DHCP (by default)
    Still must use NetEdit3.5 to see what IP parameters were assigned
  Use NetEdit3.5 for manual IP config
    Show Base Contents
    Cannot config analog
    Once IP configured, can view using web browser
Enslave using Do-more Designer (Ethernet I/O)
  Configure analog as well
    Dashboard or,
    Module Config

## Slide 28: BX-EBC100
BRX Ethernet Base Controller

## Slide 29: Configuration: BX-EBC100-M
2 models: 120-240 VAC or 12-24 VDC supply
8 expansion I/O modules
10/100 Mbps port
DIP Switches

## Slide 30: Configuration: BX-EBC100-M
IP configuration:
  DHCP (by default)
    Still must use NetEdit3.5 to see what IP parameters were assigned
  Use NetEdit3.5 for manual IP config
    Once IP configured, can view using web browser

## Slide 31: Configuration: BX-EBC100-M
Ethernet I/O:
  Enslave using Do-more Designer (Ethernet I/O)
    Configure analog as well
      Dashboard or,
      Module Config

## Slide 32: Configuration: BX-EBC100-M
Modbus TCP Server:
  Use NetEdit3.5 to:
    Configure analog
    See Modbus I/O addressing
  Use web config to:
    Configure analog
    See Modbus I/O addressing

## Slide 33: BX-MBIO
BRX Modbus I/O

## Slide 34: Configuration: BX-MBIO-M
2 models: 120-240 VAC or 12-24 VDC supply
8 expansion I/O modules
10/100 Mbps port
DIP Switches
  RTU Address

## Slide 35: Configuration: BX-MBIO-M
IP configuration:
  DHCP (by default)
    Still must use NetEdit3.5 to see what IP parameters were assigned
  Use NetEdit3.5 for manual IP config
    Once IP configured, can view using web browser

## Slide 36: Configuration: BX-MBIO-M
Modbus TCP Server:
  Use NetEdit3.5 to:
    Configure analog
    See Modbus I/O addressing
  Use web config to:
    Configure analog
    See Modbus I/O addressing

## Slide 37: Configuration: BX-MBIO-M
Modbus RTU Server:
  Uses DIP switch as serial Station ID
    If all OFF, settable via NetEdit3.5 or Web Config
  Use NetEdit3.5 or Web Config to configure serial port settings
  Must use Ethernet port to configure:
    Analog
    Serial port
    See Modbus I/O addressing

## Slide 39: MQTT (IoT)
Message Queuing Telemetry Transport
(Internet of Things)

## Slide 40: MQTT Fundamentals
MQTT Broker
Publish
Publish
Publish
Publish
Publish
Publish
Subscribe
Subscribe
Subscribe
Subscribe
Publish

## Slide 41: MQTT Terminology (1 of 2)
MQTT Broker
  Receives published topics
  Distributes topics to subscribers
  Keeps Client connections alive
  Sends Last Will & Testament (LWT) to subscribers if a Client “ungracefully disconnects”
MQTT Client
  Can publish topic(s), keep-alive time, Retain bit, QoS, Last Will & Testament
  Can subscribe to topic(s)
Topic
  Name of the data
Payload
  Actual data
Message
  Topic + Payload
QoS (Quality of Service)
  0 = At most once (BRX always, publish & subscribe): transmits message once (relies on TCP)
  1 = At least once : transmits message until it is acknowledged by receiver (may receive more than one)
  2 = Exactly once: transmits message, needs “received” message, asks if it can be “released,” needs “complete” message

## Slide 42: MQTT Terminology (2 of 2)
Publish
  To send a Topic w/Payload to MQTT Broker
Subscribe
  To request a Topic w/Payload update from MQTT Broker
Retain
  Asks MQTT Broker to save the Topic w/Payload even after sending it to all the subscribing Clients
Keep-alive Time
  How often Broker “pings” client to see if he’s there
Last Will & Testament (LWT)
  Topic w/Payload initially sent by an MQTT Client to the MQTT Broker for the Broker to send to other Clients if he is “ungracefully disconnected”

## Slide 43: MQTT Data Exchange
  Publishers are fundamentally separate from Subscribers
    Publishers only care about getting data to Broker
    Broker is fully responsible for getting data to Subscribers
  Clients connect to an MQTT Broker (TCP/IP, MQTT)
  Clients can publish data to topics, e.g.
    host/office/greg/temp, 72.3
  Clients subscribe to topics, e.g.
    host/office/greg/temp
    NOTE: MQTT supports wildcards for topics, but BRX doesn’t
  Clients receive (from Broker) all data published to topics they subscribe to
  Data can be anything (in BRX it can only be strings)
MQTT Broker
Publish
Subscribe
host/office/greg/temp

## Slide 44: MQTT Quality of Service (QoS)
0: At most once
1: At least once
2: Exactly once
BRX Uses QoS = 0 for publish & subscribe
(Lowest Bandwidth)
Basic Peer-to-peer
Financial Transactions

## Slide 45: MQTT Broker – EXAMPLE
MQTT Broker
MQTT Client #1
MQTT Client #2
MQTT Client #3
MQTT Client #4
Topic1 (data), R1
Topic2 (data), R0
LWT:
Topic3 (data), R1
Connect
CLIENT LIST:
#1-KAT:1s
Publish
TOPIC LIST:
Topic1 (data)
Topic2 (data)
LWT:
#1: Topic3 (data)
SUBSCRIBE:
No Subscribers
Connect
#3-KAT:5s
Topic1
Topic3
Subscribe
#3: T1, T3
Topic1 exists & is retained
(data)
Broker sends Topic1 to #3
Topic3 not sent because it is LWT & #1 is still alive
Connect
Topic1
Topic2
Topic6
Subscribe
#4: T1, T2, T6
(data)
Broker sends Topic1 to #4
Topic2 & Topic6 do not exist
#4-KAT:30s
Topic2 data changes so Client publishes change
Client#4 needs Topic2
(data)
Broker sends Topic2 to #4
Topic2 not retained
Topic2 not retained
Connect
#2-KAT:30s
Topic4 (data), R0
Topic5 (data), R0
Topic6 (data), R0
Publish
Topic4 (data)
Topic5 (data)
Topic6 (data)
(data)
(data)
Client#4 needs Topic6
Broker sends Topic6 to #4
Topic4, 5 & 6 not retained
Client #1 is abruptly cut off!
LWT sent to Client #3
Topic3 is retained
Topic3 is retained
If Client #1 had disconnected in a normal way: 1. Broker deletes LWT (Topic3)
2. Broker does not send Topic3 to anyone
(data)
(data)

## Slide 46: MQTT in BRX (Configuration)
Must create MQTT Client Device
Device Name
  Referenced by the MQTTPUB & MQTTSUB instructions
MQTT Server Address
  Use Server Name
    URL of Broker; will be resolved when instructions are executed
  Use IP Address
    IP address of Broker
Other Settings
  Server Port
    1883 (MQTT default)
  Comm Timeout
    How long Device will wait for response from Broker before an error
  Session Keep Alive
    Client tells Broker this time upon connection
    If Client doesn’t talk to Broker in this time period, Broker will ping him to make sure he’s still there.

## Slide 47: MQTT in BRX (Configuration)
Enable Account Authentication
  Some MQTT Brokers require authentication with Username & Password
Enable Will
  If Client is “ungracefully disconnected” from Broker, Broker will send this Topic to any Client that has subscribed to it
  Topic:
    Text name of Topic of Last Will & Testament
  Payload:
    Text of the data of the Last Will & Testament
  Retain Topic
    If this is checked, and this Client is “ungracefully disconnected,” Broker will hold this value and send it to any other Client who subscribes to the Topic in the future

## Slide 48: MQTTPUB “IoT Publish MQTT Topics”
MQTTPUB “IoT Publish MQTT Topics”
MQTT Client Device
  MQTT Device name you just created
  Enable
    Once on Leading Edge
      Makes TCP connection to Broker
      Publishes listed Topics
      Disconnects from Broker
    Continuous on Power Flow at Interval
      Constant or Variable
        Every interval, instruction scans list & does what each Topic’s Publish rule states

## Slide 49: MQTTPUB “IoT Publish MQTT Topics”
Optional Topic Prefix
  Prepended text for all Topics in list
Topic List
  Up to 50 Topics to publish
  When instruction is executed each Topic in list is published according to Publish Interval Setting rule
  Topic
    Use common Optional Topic Prefix – check to use the prepended text
    Enter a name for a Topic that makes sense to you
  Payload - Enter the string element or a literal string in quotes
  Retain – tells the MQTT server you want this Topic to be retained
    NOTE: to delete a retained Topic from the MQTT server, send another Retained Topic with an empty Payload (e.g. “”, or an empty string Element)
  Publish Interval Setting
    Publish at Interval only if value changed since the last Interval
    Publish at every Interval even if the value has not changed

## Slide 50: MQTTPUB “IoT Publish MQTT Topics”
On Success and On Error
  Set a bit, or JMP to Stage
Extended Error Information
  Must be a double-word
    Upper word contains entry number of the first Topic that failed (e.g. D0:W1)
    Lower word contains error code (e.g. D0:W0)
Ladder Stage editing helper
  Automatically create the SG box for any NEW stage number – if either of the On Success or On Error selection is “JMP to Stage” this option can be checked
    Below this rung
    At end of code-block
VALUE | ERROR | DESCRIPTION
0 | <none> | <none>
57 | Unexpected MQTT Response | MQTT Broker response not properly formed
58 | MQTT Broker rejected | MQTT Broker refused Topic (Username? Password? Security violation?)
59 | Out of resources (MQTTSUB only) | > 10 MQTTSUBs or > 100 Topics using same MQTT Client device
60 | Invalid Topic | Topic is empty
61 | Duplicate Topic | Topic already subscribed to in different MQTTSUB

## Slide 51: MQTTSUB “IoT Subscribe MQTT Topics”
MQTTSUB “IoT Subscribe MQTT Topics”
MQTT Client Device
  MQTT Device name you just created
  Enable to subscribe to Topics in the Topic list, and keep enabled for them to constantly update

## Slide 52: MQTTSUB “IoT Subscribe MQTT Topics”
Optional Topic Prefix
  Prepended text for all Topics in list
Topic List
  Up to 50 Topics to subscribe to
  Topic
    Use common Optional Topic Prefix – check to use the prepended text
    Enter a name for a Topic you want to subscribe to
  Payload - enter the string Element where the Topic’s data will be stored

## Slide 53: MQTTSUB “IoT Subscribe MQTT Topics”
Instruction Operation
  When 1st enabled:
    On Success & On Error bits are turned OFF
      NOTE: Instruction must remain enabled for all subscribed Topics to keep updating.
    Attempts to subscribe to all Topics
      If > 0 successfully subscribed then On Success bit comes ON
      If all subscriptions failed then On Error bit comes ON
  While kept enabled:
    Continuously updates all Topics it receives from MQTT Broker
      NOTE: It does NOT try to re-subscribe to Topics that may have failed initially
  When disabled:
    Attempts to unsubscribe from all Topics
      If > 0 successfully unsubscribed then On Success bit comes ON
      If all Topics failed to unsubscribe then On Error bit comes ON
    If no other MQTTSUB or MQTTPUB instructions are using the MQTT Client Device, then it will cause the MQTT Client to disconnect from the MQTT Broker (TCP disconnect)
Extended Error Information is same as MQTTPUB