## Slide 1: BRX Technical Training
Onboard Input Digital Filtering

## Slide 2: Onboard Input Filters
BX10
  6 discrete IN (all high-speed)
    Digitally filtered
  4 discrete OUT (2 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX10E
  6 discrete IN (all high-speed)
    Digitally filtered
  4 discrete OUT (2 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 3: Onboard Input Filters
BX18
  10 discrete IN (all high-speed)
    Digitally filtered
  8 discrete OUT (4 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX18E
  10 discrete IN (all high-speed)
    Digitally filtered
  8 discrete OUT (4 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 4: Onboard Input Filters
BX36
  20 discrete IN (10 high-speed)
    Digitally filtered
  16 discrete OUT (8 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX36E
  20 discrete IN (10 high-speed)
    Digitally filtered
  16 discrete OUT (8 high-speed)
  4 analog IN
  2 analog OUT
  Ethernet port

## Slide 5: Onboard Input Filters
Purpose
  Switch bounce
  Electrical noise
Solution
  Low-pass filter
Cleaner solution:
  Digital low-pass filter

## Slide 6: Onboard Input Filters
Digital Filtering
  Input state determined every clock tick
  System clock is 75MHz thus every 1/75MHz = 13.33ns
  Digital filtering is just a counter
    If the hardware circuitry sees the input as ON, counter increments by 1
    If the hardware circuitry sees the input as OFF, counter decrements by 1
    When counter reaches number of raw clock counts preset in filter value, the input is seen as ON
3 ways to enter the filter value