## Slide 1: BRX Technical Training
High-Speed I/O (Axis & Pulse Outputs)

## Slide 2: High-Speed I/O
BX10
  6 discrete IN (all high-speed)
  4 discrete OUT (2 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX10E
  6 discrete IN (all high-speed)
  4 discrete OUT (2 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 3: High-Speed I/O
BX18
  10 discrete IN (all high-speed)
  8 discrete OUT (4 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX18E
  10 discrete IN (all high-speed)
  8 discrete OUT (4 high-speed)
  1 analog IN
  1 analog OUT
  Ethernet port

## Slide 4: High-Speed I/O
BX36
  20 discrete IN (10 high-speed)
  16 discrete OUT (8 high-speed)
  No analog IN
  No analog OUT
  No Ethernet port
BX36E
  20 discrete IN (10 high-speed)
  16 discrete OUT (8 high-speed)
  4 analog IN
  2 analog OUT
  Ethernet port

## Slide 5: High-Speed Outputs (Axis)
Default Device Name: @Axis0, 1, 2 & 3
Default Structure: $Axis0, 1, 2 & 3
Virtual – configured only with AXCONFIG instruction; no actual physical I/O is used
  @Axis0 is only a virtual axis
  @Axis1-3 can be virtual (by default) but can also be configured to drive physical high-speed outputs

## Slide 6: High-Speed Outputs (Axis)
Pulse Output Configuration
  Step/Direction (2 outputs)
    1 for step pulses
    1 for selecting direction
  CW/CCW (2 outputs)
    1 for clockwise pulses
    1 for counter-clockwise pulses
  Quadrature (2 outputs)
    1 for A output
    1 for B output

## Slide 7: High-Speed Outputs (Axis)
Instructions:
  AXCONFIG “Axis Configuration”
  AXJOG “Axis Jog Mode”
  AXVEL “Axis Set Velocity Mode”
  AXHOME “Axis Perform Home Search”
  AXPOSTRAP “Axis Move to Position Using Trapezoid”
  AXPOSSCRV “Axis Move to Position Using S-Curve”
  AXGEAR “Axis Electronic Gearing”
  AXFOLLOW “Axis Position Following with Offset”
  AXCAM “Axis Electronic Camming”
  AXRSTFAULT “Reset Axis Limit Fault”
  AXSETPROP “Set Axis Properties”

## Slide 8: High-Speed Outputs (Axis)
AXCONFIG “Axis Configuration”
  Pick Device Name
  Can configure axis directly from the instruction using the <Configure Axis…> button
  Linear vs Rotary
    Linear moves forward or backward along a linear path
    Rotary revolves so the position stays within a defined range; usually related to 360° of motion
Position: 0 (home)
Position: +100,000
Position: 0° (home)
Position: 90°
Position: 180°
Position: 270°

## Slide 9: High-Speed Outputs (Axis)
AXCONFIG “Axis Configuration” (continued)
  These are the main parameters
  Initial Output Position – when the Axis is first enabled, this will be the current position value
  Minimum Velocity – slowest frequency of output
  Maximum Velocity – fastest frequency of output
  Acceleration – rate of acceleration
  Deceleration – rate of deceleration
  Fault Deceleration – any time a Fault Limit is reached or the Axis’ Master Enable is manually turned OFF, the Axis will decelerate to stop using this rate; if 0 (zero), then pulses will stop immediately

## Slide 10: High-Speed Outputs (Axis)
AXCONFIG “Axis Configuration” (continued)
  Enable this if using an encoder for feedback
  If used for position feedback the Axis’ .FollowingError = difference between the output pulse count (.TargetPosition) and the encoder input value (.CurrentPosition)
    If this number keeps increasing there is a problem
  Pick the encoder: High Speed Input Function 1 ($HsCtrTmr1.Acc), etc.
  Can configure the counter from the instruction using the <Configure High Speed Input…> button
  Position Based on
    Encoder – uses the encoder’s current value for Axis position
    Pulse Output – uses output pulse count for Axis position
  Pulse Output/Encoder Scale Factor – enter scaling factor for the application (e.g. motor’s ppr / encoder ppr; or there could be mechanical gearing, etc.)
  Encoder Deadband (counts) – value that is applied above and below the encoder value; helps prevent “seeking”

## Slide 11: High-Speed Outputs (Axis)
AXCONFIG “Axis Configuration” (continued)
  Enable these if you have a limit switch/sensor for this purpose
  When these inputs are activated it will cause the Axis to go into a fault and decelerate to a stop
    Monitor .Fault
    To reset the fault:
      Use AXRSTFAULT instruction, or…
      Use AXCONFIG instruction to reconfigure Axis

## Slide 12: High-Speed Outputs (Axis)
AXJOG “Axis Jog Mode”
  Allows the manual adjustment of an Axis’ position
  Uses the acceleration and deceleration parameters setup in the AXCONFIG instruction
  Maximum velocity is determined by either the Maximum Velocity specified here or in the AXCONFIG instruction; whichever is lower
  Can zero the count after adjustment (e.g. a manual homing)
  Input legs:
    E/R – Enable/Reset; when ON Axis is in jog mode
    FW – Forward; move Axis forward
    RV – Reverse; move Axis in reverse
    If both FW & RV are ON, Axis decelerates to stop
  Success or Error on come on when E/R goes OFF

## Slide 13: High-Speed Outputs (Axis)
AXVEL “Axis Set Velocity Mode”
  Allows Axis to be put in velocity mode where movement is controlled by velocity (vs position)
  .TargetVelocity can be changed on-the-fly
  Uses AXCONFIG parameters unless otherwise selected
  Can use an initial velocity when the instruction is enabled
  Can select acceleration / deceleration mode:
    Trapezoid
    S-Curve
      Jerk parameter
    Instantaneous
  Can use different acceleration / deceleration than AXCONFIG
  Success or Error only come on when E/R leg goes OFF

## Slide 14: High-Speed Outputs (Axis)
AXHOME “Axis Perform Home Search”
  Performs homing function to move Axis to physical starting position
  Homing Velocity – sign determines direction
  Choose input for home switch (Limit 1)
  Choose termination
    Position – an offset from the home switch (sign determines direction)
    Creep to Second Limit – can be the same input; Creep Velocity’s sign determines direction
    Decelerate to 0 Velocity
  Choose where zero position is
  Input leg can be Edge triggered or Power flow enabled
    Use Power Flow if you might want to abort the operation with the input leg logic
  Success or Error only occurs after homing is complete

## Slide 15: High-Speed Outputs (Axis)
AXPOSTRAP “Axis Move to Position Using Trapezoid”
  Causes Axis to move to a Position Value via an absolute or relative position value
  Uses AXCONFIG parameters unless superseded here
  Works with linear or rotary axes
  Can also be a multi- move instruction using the Update Target Position bit

## Slide 16: High-Speed Outputs (Axis)
AXPOSTRAP “Axis Move to Position Using Trapezoid” (continued)
  Move Type
    Single move – one move is executed when input leg is either:
      Edge triggered, or…
      Power flow enabled – use this if you want to abort (causing a fault) during the move using the input leg logic
    Multi-move – multiple moves are possible using the following bit and the Position Value (variable)
      Update Target Position bit
        Write new position to Position Value variable
        Set Update Target Position bit ON
        AXPOSTRAP will reset Update Target Position bit OFF when new position is recognized
        Wait for .AtPosition bit to come ON

## Slide 17: High-Speed Outputs (Axis)
AXPOSTRAP “Axis Move to Position Using Trapezoid” (continued)
  Target Type
    Absolute – Position Value is measured from the Axis’ zero position
    Relative – Position Value is measured from the Axis’ .CurrentPosition
    Zero out .CurrentPosition before initial run
      If Single Move Type, zeroed out before the move
      If Multi-move Type, zeroed on the first move only

## Slide 18: High-Speed Outputs (Axis)
AXPOSTRAP “Axis Move to Position Using Trapezoid” (continued)
  Rotary (Absolute)
    Clockwise only
    Counterclockwise only
    Shortest Direction
  Rotary (Relative)
    Sign of Position Value is direction
    Zero-out .Current Position before initial run

## Slide 19: High-Speed Outputs (Axis)
AXPOSTRAP “Axis Move to Position Using Trapezoid” (continuted)
  Supersede Default Properties – pick which ones to use; indicated by red graphic color
    Maximum Velocity
    Acceleration
    Deceleration
  Success or Error come on:
    After a Single Move is complete
    If a Multi-Move Type; after the input leg loses power flow

## Slide 20: High-Speed Outputs (Axis)
AXPOSSCRV “Axis Move to Position Using S-Curve”
  Almost identical to AXPOSTRAP except:
    No multi-moves are allowed
    Jerk parameter required (rate of change of acceleration / deceleration)

## Slide 21: High-Speed Outputs (Axis)
AXGEAR “Axis Electronic Gearing”
  Creates a Master / Slave connection that will synchronized the movement of one Axis to another Axis or a High-Speed Counter / Timer.
  If velocity-centric:
    Slave's velocity is derived from the Master's velocity (adjusted by gear ratio)
    Gear Ratio and the Master's Target Velocity can be changed on-the-fly
  If position-centric:
    Slave's position is derived from the Master position (modified by Gear Ratio)
    Changes to Gear Ratio and the Master's Target Position on-the-fly are ignored
  Use .MstSlvCoordError to monitor the difference between the Master Axis' position and the Slave Axis' position

## Slide 22: High-Speed Outputs (Axis)
AXGEAR “Axis Electronic Gearing” (continued)
  Maser Register
    Axis0-3 Position
    High-Speed Counter / Timer 1-3 Acc
  Non-Axis Master Filter Time – only for Counter / Timer inputs; how often Slave’s position is calculated
  Gear Ratio Multiplier - multiplier applied to Slave's position or velocity; 0 (zero) means stop; negative values cause opposite motion

## Slide 23: High-Speed Outputs (Axis)
AXFOLLOW “Axis Position Following with Offset”
  Similar to AXGEAR except:
    Can go to an offset relative position
    Can use an offset relative velocity
  Causes an Axis to follow a Master’s movement (another Axis or a High- Speed Counter / Timer
  Follower Axis needs to overtake the Master Axis if a Goto Relative Offset is commanded so Follower’s Maximum Velocity and Acceleration & Deceleration parameters need to be larger than the Master’s
  Use .MstSlvCoordError to monitor the difference between the Master Axis' position and the Slave Axis' position

## Slide 24: High-Speed Outputs (Axis)
AXFOLLOW “Axis Position Following with Offset” (continued)
  Relative Offset Position – Follower's position will be adjusted by this pulse count value each time the Goto Offset Signal turns ON
  Relative Offset Velocity – additional velocity (relative to the Master’s velocity) the Follower will use when moving to the Relative Offset Position
  Goto Offset Signal - each time this bit comes ON the Follower will attempt to move to the Relative Offset Position using the Relative Offset Velocity
    When Follower reaches Relative Offset Position this bit is turned OFF
    If it stays ON then the Follower can’t catch up to the Master
      Adjust for higher maximum velocity and/or faster acceleration / deceleration

## Slide 25: High-Speed Outputs (Axis)
AXCAM “Axis Electronic Camming”
  Causes an Axis to synchronize its movement to a Master Axis so that its position corresponds to values in the cam table
  Cam Tables can be located right in the instruction, or in PLC memory
    There is a configurator dialog to aid in creating Cam Tables in memory
  Cam Tables can have up to 64 points
  Uses “Cubic Interpolation” to generate a trajectory between each pair of entries in the table
  The CPU will fit a smooth curve to the data which will pass through every point in the table

## Slide 26: High-Speed Outputs (Axis)
AXCAM “Axis Electronic Camming” (continued)
  Master Position Offset – added to the Master Axis position before the associated Slave position value is calculated (cam table can start at an offset)
    Table graph will display the value
  Load Slave Curve Fitting Points from Data Block – choose this if the cam table is located in PLC memory
    Length from Starting Master Position - total number of pulse counts the Master will move
    Number of Curve Fitting Points - number of equal-length segments the Length from Master Position will be divided into; 3-64
    Slave Curve Fitting Table Starting Address - PLC memory address
    Use the <PLC AXCAM Curve Fitting Editor...> button if online to the PLC to generation the table in memory

## Slide 27: High-Speed Outputs (Axis)
AXCAM “Axis Electronic Camming” (continued)

## Slide 28: High-Speed Outputs (Axis)
AXCAM “Axis Electronic Camming” (continued)
  Fixed Curve Fitting Points – choose this if the cam table is located in the instruction itself
    Length from Starting Master Position
    Number of Curve Fitting Points
    Use the <Apply to table> button to graph the changes
  Enable Relative Mode – if enabled then when the instruction is enabled, the Slave Axis' current position is stored internally and becomes the new 0 (zero) for the Slave Axis

## Slide 29: High-Speed Outputs (Axis)
AXCAM “Axis Electronic Camming” (continued)
  Green – velocity offset
  Blue – position offset
  Red – data points from table

## Slide 30: High-Speed Outputs (Axis)
AXRSTFAULT “Reset Axis Limit Fault”
  Clears the fault of an Axis that has either:
    Triggered one of its Fault Limits, or…
    Has had its .MasterEnable manually turned OFF
  After clearing the fault any move in the same direction that caused the fault will immediately generate another fault condition
  AXCONFIG instruction will also reset an Axis that is in a fault state

## Slide 31: High-Speed Outputs (Axis)
AXSETPROP “Set Axis Properties”
  Used to make changes to some of the configured parameters of an Axis without having to re-run an AXCONFIG
  Changes made are reflected in all subsequent instructions that reference this Axis
  Changes will not affect any Axis instructions that are currently running

## Slide 32: High-Speed Outputs (Axis)
Axis ($Axis0, 1, 2 & 3) Structure members:
  .TargetVelocity (signed DW; R/W) – velocity (pps) the Axis is accelerating / decelerating toward
  .CurRateOfChg (signed DW; R/W) – current velocity (pps) being used during acceleration / deceleration
  .TargetPosition (signed DW; RO) – pulse count the Axis is moving toward
  .CurrentVelocity (signed DW; RO) – current velocity (pps) of the Axis
  .CurrentPosition (signed DW; RO) – current position (pulse count) of the Axis
  .FollowingError (signed DW; RO) – when using encoder feedback as Axis position, this value (in pulse counts; not encoder counts) is the difference between the output pulse count (.TargetPosition) and the encoder input value (.CurrentPosition)
    Large increasing value could indicate:
      Motor stalled
      Mechanical slippage
      Filter Time Constant is too large
      Resolution of encoder is too small

## Slide 33: High-Speed Outputs (Axis)
Axis ($Axis0, 1, 2 & 3) Structure members (continued):
  .MstSlvCoordError (signed DW; RO) – when a slave axis in AXGEAR, a follower in AXFOLLOW mode, or a slave in AXCAM mode, value (pulse counts, not encoder counts) is difference between the position of the master axis and the projected location of the slave axis; negative value means it is behind; positive value means it is ahead
  .Suspend (bit; R/W) – set ON to cause axis to decelerate to stop using the Axis’ deceleration rate; reset OFF to cause axis to acceleration back to .TargetVelocity
  .MasterEnable (bit; R/W) – automatically set ON when axis is properly configured; reset OFF to cause axis to decelerate to stop using the axis’ Fault Deceleration Rate; use AXRSTFAULT or AXCONFIG to clear the fault
  .EnableOutput (bit; R/W) – automatically set ON when the Axis is properly configured; reset OFF to cause axis to immediately stop (no deceleration rate)
  .Configured (bit; RO) - ON if an AXCONFIG has successfully executed
  .Active (bit; RO) - ON any time the Axis is enabled and in any mode other than idle
  .AtVelocity (bit; RO) - ON when .TargetVelocity = .CurrentVelocity
  .AtPosition (bit; RO) - ON when .TargetPosition = .CurrentPosition
  .ScriptBusy (bit; RO) - ON when the Axis is running a script (reserved)

## Slide 34: High-Speed Outputs (Axis)
Axis ($Axis0, 1, 2 & 3) Structure members (continued):
  .Fault (bit; RO) - ON when:
    Fault Limit has been triggered, or…
    If Axis' .MasterEnable has been manually turned OFF
    AXRSTFAULT or an AXCONFIG must be executed to reset OFF
  .Mode (unsigned byte; RO) - execution mode
    00 (Unconfigured) 130 (Smart Position)
    01 (Idle) 131 (Electronic Gearing)
    65 (Positive Limit Fault) 132 (Follower)
    66 (Negative Limit Fault) 133 (Cam)
    67 (Fault Both Limits) 134 (Terminate)
    68 (Fault Master Enable) 135 (S-Curve Velocity)
    128 (Velocity) 136 (S-Curve-Terminate)
    129 (Smart Velocity)