## Slide 1: Do-more Technical Training
Communications
(Custom Serial)

## Slide 2: Communications – Custom Serial
Do-more built-in serial port
Do-more with SERIO/SERIO4

## Slide 3: Communications – Custom Serial
Serial & TCP Protocols are streams of data
Serial medium is usually a private conversation
I need to give you the latest data on the weather.
ENGINEERING: What type of data will be sent?
OK, but don’t talk too slow; I’ve got other things to do.
ENGINEERING: How is the data transmitted?
OK. I will talk at this rate and only to you.
How will I know when the conversation is complete?
ENGINEERING: How will the data end?
I’ll say ‘bye’.
I’m only going to give you 5 data points.
OK, I’m listening…
IMPLIMENTATION: Partner listens.
Stream of weather data…
Bye
IMPLIMENTATION: Transfer complete
Thanks.
IMPLIMENTATION: (Processes data)

## Slide 4: Communications – Custom Serial
TCP Protocol medium is a network
TCP is connection-based protocol
Dial
Ring
A “connection” must be established before a conversation can take place. The client (man) must call the server (woman). One is initiating and the other is listening.
Hello?
Can we talk?
I’m sorry, but I’m pretty busy at the moment.
OK. I’ll call you later.
Dial
Ring
Hello?
Can we talk?
Sure. What’s up?
<starts conversation>
The conversation is delimited because both parties will agree on when it is over and say, “Bye”, just like serial comms.

## Slide 5: Communications – Custom Serial
UDP Protocol medium is also a network
UDP is connectionless protocol
Since no connection is needed, no resources (i.e. cellphone) are monopolized
A “connection” is not necessary. The client (man) simply sends a message to the server (woman).

## Slide 6: Communications – Custom Serial
Custom Protocol | Type | Data Size | Client Instruction | Server Instruction | Server Member
Serial | Stream | Unlimited | STREAMOUT | STREAMIN | InQueue (# of bytes)
 |  |  | STREAMIN | STREAMOUT | 
TCP |  |  | OPENTCP | TCPLISTEN | 
 |  |  | STREAMOUT | STREAMIN | 
 |  |  | STREAMIN | STREAMOUT | 
UDP | Packet | 1 packet | PACKETOUT | PACKETIN | PacketAvailable (bit)

## Slide 7: Communications – Custom Serial
General Purpose comms (Initiator/Listener)
  Do-more CPU with built-in serial port or SERIO/SERIO4
    Serial Port Mode must be configured
      Use CPU Configuration for built-in or Module Configuration for SERIO/SERIO4
      Select “General Purpose”
      Use <Device Settings> button to change port settings as desired
    Use STREAMOUT (write) & STREAMIN (read) instructions

## Slide 8: Communications – Custom Serial
@IntSerial (Initiator)
@IntSerial (Listener)
“TIME” <CR><LF>
Output Buffer
“TIME”<CR><LF>
Input Buffer
“TIME”<CR><LF>
STREAMOUT
“TIME”<CR><LF>
InQueue = 6
STREAMIN
Memory
InQueue = 0
“TIME”<CR><LF>
STREAMOUT does not send data out on the wire; it merely writes the data to the @IntSerial Device’s Output Buffer
When the @IntSerial Device “gets around to it”, it sends the data in its Output Buffer out on the wire
The data goes into the @IntSerial Device’s Input Buffer where it will stay until a STREAMIN is executed to get the data out
@IntSerial Device’s structure member, InQueue, is set to indicate how many bytes are currently in the Input Buffer
The logic for the STREAMIN can be set to monitor the InQueue value & when it is executed, will read the data out of the Input Buffer

## Slide 9: Communications – Custom Serial
STREAMOUT “Stream Out Data to Device”
  Writes data from to stream-capable device
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – stream-capable Device
    Data Source:
      String Structure – string to send
      Numeric Data Block
        Buffer Start – location of start of data buffer to send
        Number of Bytes to Output
    Endian Settings:
      Swap Byte
      Swap Word
    Flush INPUT device first
    On Success: Set bit, JMP to Stage
    On Error: Set bit, JMP to Stage

## Slide 10: Communications – Custom Serial
STREAMIN “Stream in Data from Device”
  Reads data from a stream-capable device
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – stream-capable Device
    Complete when…
      Length is x bytes OR
      Delimeter(s) received OR
        Number of delimiters
        Delimiter characters
        Exact sequence
        Any one delimiter(s)
        Trim Delimiter(s) from Output String
      Network Timeout
      <Advanced…> button
    Data Destination
      String Structure
      Numeric Data Block
        Start Address
        Buffer Size in Bytes
        Number of Bytes Read
    Endian Settings: Swap Byte, Swap Word
    On Success/On Error: Set bit, JMP to Stage
When attempting to get a STREAMIN to work the first time, the importance of Network Timeout cannot be overstressed because without it the STREAMIN has potential to lock the streaming Device

## Slide 11: Communications – Custom Serial
Do-more CPU
STREAMOUT
@IntSerial
Do-more CPU
Memory
@IntSerial
General Purpose (Initiator)
General Purpose (Listener)
STREAMIN
Memory

## Slide 12: Communications – Custom Serial
Communications Test
  Commands delimited by <CR><LF>:
    TIME
      Response: “Current PLC Time is: 04:02:14 PM”
    DATE
      Response: “Current PLC Date is: 3/11/2016”
    SCANTIME
      Response: “Current PLC Scan Time is: 561us”
    FIRMWARE
      Response: “Current PLC Firmware is: 176201”
    IPADDRESS
      Response: “Current PLC IP Address is: 10.1.1.200”