## Slide 1: Do-more Technical Training
Communications
(Custom TCP)

## Slide 2: Communications – Custom TCP
Do-more built-in Ethernet

## Slide 3: Communications – Custom TCP
Serial & TCP Protocols are streams of data
Serial medium is usually a private conversation
I need to give you the latest data on the weather.
ENGINEERING: What type of data will be sent?
OK, but don’t talk too slow; I’ve got other things to do.
ENGINEERING: How is the data transmitted?
OK. I will talk at this rate and only to you.
How will I know when the conversation is complete?
ENGINEERING: How will the data end?
I’ll say ‘bye’.
I’m only going to give you 5 data points.
OK, I’m listening…
IMPLIMENTATION: Partner listens.
Stream of weather data…
Bye
IMPLIMENTATION: Transfer complete
Thanks.
IMPLIMENTATION: (Processes data)

## Slide 4: Communications – Custom TCP
TCP Protocol medium is a network
TCP is connection-based protocol
Dial
Ring
A “connection” must be established before a conversation can take place. The client (man) must call the server (woman). One is initiating and the other is listening.
Hello?
Can we talk?
I’m sorry, but I’m pretty busy at the moment.
OK. I’ll call you later.
Dial
Ring
Hello?
Can we talk?
Sure. What’s up?
<starts conversation>
The conversation is delimited because both parties will agree on when it is over and say, “Bye”, just like serial comms.

## Slide 5: Communications – Custom TCP
UDP Protocol medium is also a network
UDP is connectionless protocol
Since no connection is needed, no resources (i.e. cellphone) are monopolized
A “connection” is not necessary. The client (man) simply sends a message to the server (woman).

## Slide 6: Communications – Custom TCP
TCP Client (Master/Initiator)
  Do-more CPU with built-in Ethernet port
    Must create a TCP Client Device
      Use Device Configuration & <New Device> button  “TCP Client”, press <OK> button
      Give it a Device Name
    Use the OPENTCP instruction to establish connection to partner (Server/Slave)
    Use STREAMOUT/STREAMIN instructions to send/receive data to/from partner (Server/Slave)

## Slide 7: Communications – Custom TCP
TCP Server (Slave/Listener)
  Do-more CPU with built-in Ethernet port
    Must create a TCP Server Device
      Use Device Configuration & <New Device> button  “TCP Server”, press <OK> button
      Give it a Device Name & TCP Port number
    Use the TCPLISTEN instruction to listen for connection request from partner (Client/Master)
    Use STREAMIN/STREAMOUT instructions to send/receive data to/from partner (Client/Master)

## Slide 8: Communications – Custom TCP
Custom Protocol | Type | Data Size | Client Instruction | Server Instruction | Server Member
Serial | Stream | Unlimited | STREAMOUT | STREAMIN | InQueue (# of bytes)
 |  |  | STREAMIN | STREAMOUT | 
TCP |  |  | OPENTCP | TCPLISTEN | 
 |  |  | STREAMOUT | STREAMIN | 
 |  |  | STREAMIN | STREAMOUT | 
UDP | Packet | 1 packet | PACKETOUT | PACKETIN | PacketAvailable (bit)

## Slide 9: Communications – Custom TCP
@MyTCPClient (Master)
@MyTCPServer (Slave)
OPENTCP
TCPLISTEN
OPENTCP must be enabled in order for the connection request to be sent to the Server/Slave
Establish TCP Connection
TCP/IP
SYN
If Server does not respond in 15 seconds (not configurable) the OPENTCP instruction errors out
TCPLISTEN must be enabled in order for the Server (Slave) to listen for the connection request
SYN, ACK
ACK
TCP Connection Established
TCP Connection
Established
Output Buffer
“TIME”<CR><LF>
Input Buffer
“TIME”<CR><LF>
STREAMOUT
“TIME”<CR><LF>
STREAMOUT does not send data out on the wire; it merely writes the data to the @MyTCPClient Device’s Output Buffer
When the @MyTCPClient Device “gets around to it”, it sends the data in its Output Buffer out on the wire
InQueue = 0
“TIME” <CR><LF>
The data goes into the @MyTCPServer Device’s Input Buffer where it will stay until a STREAMIN is executed to get the data out
InQueue = 6
@MyTCPServer Device’s structure member, InQueue, is set to indicate how many bytes are currently in the Input Buffer
STREAMIN
Memory
The logic for the STREAMIN can be set to monitor the InQueue value & when it is executed, will read the data out of the Input Buffer
“TIME”<CR><LF>

## Slide 10: Communications – Custom TCP
OPENTCP “Open TCP Connection”
  Opens TCP Client Device & attempts to establish a TCP connection to a TCP server device
  Structure member Open comes ON when the TCP Client is opened
  Structure member Connected comes ON when the TCP Server responds with a connection acknowledgement
  Fully asynchronous instruction (red triangle)
  Parameters:
    TCP Device – TCP client Device
    To IP Address: TCP server’s IP address
      Variable Address or Fixed Address
    TCP Port Number
    On Success: Set bit, JMP to Stage
    On Error: Set bit, JMP to Stage

## Slide 11: Communications – Custom TCP
TCPLISTEN “Start Listening on TCP Port”
  Listens for a TCP Client connection request & then runs a Program
  Structure member Connected comes ON when a connection request is acknowledged
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – TCP Server Device
    On connect, run Program: name of the Program that will run whenever a TCP connection from a TCP Client has been made successfully

## Slide 12: Communications – Custom TCP
STREAMOUT “Stream Out Data to Device”
  Writes data from to stream-capable device
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – stream-capable Device
    Data Source:
      String Structure – string to send
      Numeric Data Block
        Buffer Start – location of start of data buffer to send
        Number of Bytes to Output
    Endian Settings:
      Swap Byte
      Swap Word
    Flush INPUT device first
    On Success: Set bit, JMP to Stage
    On Error: Set bit, JMP to Stage

## Slide 13: Communications – Custom TCP
STREAMIN “Stream in Data from Device”
  Reads data from a stream-capable device
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – stream-capable Device
    Complete when…
      Length is x bytes OR
      Delimeter(s) received OR
        Number of delimiters
        Delimiter characters
        Exact sequence
        Any one delimiter(s)
        Trim Delimiter(s) from Output String
      Network Timeout
      <Advanced…> button
    Data Destination
      String Structure
      Numeric Data Block
        Start Address
        Buffer Size in Bytes
        Number of Bytes Read
    Endian Settings: Swap Byte, Swap Word
    On Success/On Error: Set bit, JMP to Stage
When attempting to get a STREAMIN to work the first time, the importance of Network Timeout cannot be overstressed because without it the STREAMIN has potential to lock the streaming Device

## Slide 14: Communications – Custom TCP
Do-more CPU
STREAMOUT
TCP/IP
@TCPClnt
Do-more CPU
Memory
@TCPSrv
TCP Client (Initiator)
TCP Server (Listener)
STREAMIN
Memory
OPENTCP
TCPLISTEN

## Slide 15: Communications – Custom TCP
Communications Test
  IP Address: 10.1.1.200
  TCP/IP Port #: 5678
  Commands delimited by <CR><LF>:
    TIME
      Response: “Current PLC Time is: 04:02:14 PM”
    DATE
      Response: “Current PLC Date is: 3/11/2016”
    SCANTIME
      Response: “Current PLC Scan Time is: 561us”
    FIRMWARE
      Response: “Current PLC Firmware is: 176201”
    IPADDRESS
      Response: “Current PLC IP Address is: 10.1.1.200”