## Slide 1: Do-more Technical Training
Communications
(Custom UDP)

## Slide 2: Communications – Custom UDP
Do-more built-in Ethernet

## Slide 3: Communications – Custom UDP
Serial & TCP Protocols are streams of data
Serial medium is usually a private conversation
I need to give you the latest data on the weather.
ENGINEERING: What type of data will be sent?
OK, but don’t talk too slow; I’ve got other things to do.
ENGINEERING: How is the data transmitted?
OK. I will talk at this rate and only to you.
How will I know when the conversation is complete?
ENGINEERING: How will the data end?
I’ll say ‘bye’.
I’m only going to give you 5 data points.
OK, I’m listening…
IMPLIMENTATION: Partner listens.
Stream of weather data…
Bye
IMPLIMENTATION: Transfer complete
Thanks.
IMPLIMENTATION: (Processes data)

## Slide 4: Communications – Custom UDP
TCP Protocol medium is a network
TCP is connection-based protocol
Dial
Ring
A “connection” must be established before a conversation can take place. The client (man) must call the server (woman). One is initiating and the other is listening.
Hello?
Can we talk?
I’m sorry, but I’m pretty busy at the moment.
OK. I’ll call you later.
Dial
Ring
Hello?
Can we talk?
Sure. What’s up?
<starts conversation>
The conversation is delimited because both parties will agree on when it is over and say, “Bye”, just like serial comms.

## Slide 5: Communications – Custom UDP
UDP Protocol medium is also a network
UDP is connectionless protocol
Since no connection is needed, no resources (i.e. cellphone) are monopolized
A “connection” is not necessary. The client (man) simply sends a message to the server (woman).

## Slide 6: Communications – Custom UDP
UDP Connection (Initiator or Listener)
  Do-more CPU with built-in Ethernet port
    Must create a UDP Connection
      Use Device Configuration & <New Device> button  “UDP Connection”, press <OK> button
      Give it a Device Name
      Give it a UDP Port number – this Device will only receive packets that are sent to this port number
    Use PACKETOUT / PACKETIN instructions to send/receive data to/from partner

## Slide 7: Communications – Custom UDP
Custom Protocol | Type | Data Size | Client Instruction | Server Instruction | Server Member
Serial | Stream | Unlimited | STREAMOUT | STREAMIN | InQueue (# of bytes)
 |  |  | STREAMIN | STREAMOUT | 
TCP |  |  | OPENTCP | TCPLISTEN | 
 |  |  | STREAMOUT | STREAMIN | 
 |  |  | STREAMIN | STREAMOUT | 
UDP | Packet | 1 packet | PACKETOUT | PACKETIN | PacketAvailable (bit)

## Slide 8: Communications – Custom UDP
@MyUDP (Initiator)
@MyUDP (Listener)
“TIME” <CR><LF>
Output Buffer
“TIME”<CR><LF>
Input Buffer
“TIME”<CR><LF>
PACKETOUT
“TIME”<CR><LF>
PacketAvailable = ON
PACKETIN
Memory
PacketAvailable = OFF
“TIME”<CR><LF>
PACKETOUT does not send data out on the wire; it merely writes the data to the @MyUDP Device’s Output Buffer
When the @MyUDP Device “gets around to it”, it sends the data in its Output Buffer out on the wire
The data goes into the @MyUDP Device’s Input Buffer where it will stay until a PACKETIN is executed to get the data out
@MyUDP Device’s structure member, PacketAvailable, is set ON indicate one or more packets are currently in the Input Buffer
The logic for the PACKETIN can be set to monitor the PacketAvailable bit & when it is executed, will read the data out of the Input Buffer

## Slide 9: Communications – Custom UDP
PACKETOUT “Output Data to Packet Device”
  Writes data to UDP Device’s output buffer
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – UDP Connection Device
    To IP Address:
      Variable Address From UDP Read – uses IP address read from the last PACKETIN instruction execution
      Fixed Address
    To UDP Port Number
    Data Source:
      String Structure – string to send
      Numeric Data Block
        Buffer Start – location of start of data buffer to send
        Number of Bytes to Output
    On Success: Set bit, JMP to Stage
    On Error: Set bit, JMP to Stage

## Slide 10: Communications – Custom UDP
PACKETIN “Input Data from Packet Device”
  Retrieves data from UDP Device’s input buffer
  Structure member PacketAvailable comes ON when there is one or more packets in the input buffer to receive
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device – UDP Connection Device
    Came from IP Address – where to put the sender’s IP address from which the packet came from
    Came from UDP Port Number – where to put the packet’s sending port number value
    Network Timeout
    Max Number of Bytes to read from Packet
    Data Destination:
      String Structure
      Numeric Data Block:
        Start Address
        Number of Bytes Read
    On Success: Set bit, JMP to Stage
    On Error: Set bit, JMP to Stage
When attempting to get a PACKETIN to work the first time, the importance of Network Timeout cannot be overstressed because without it the PACKETIN has potential to lock the UDP Device
The Came from IP Address & Came from UDP Port Number parameters are NOT something you provide, but instead are something the PACKETIN instruction provides you

## Slide 11: Communications – Custom UDP
Do-more CPU
PACKETOUT
UDP
@MyUDP
Do-more CPU
Memory
@MyUDP
UDP Connection (Initiator)
UDP Connection (Listener)
PACKETIN
Memory

## Slide 12: Communications – Custom UDP
Communications Test
  IP Address: 10.1.1.200
  UDP Port #: 1234
  Commands delimited by <CR><LF>:
    TIME
      Response: “Current PLC Time is: 04:02:14 PM”
    DATE
      Response: “Current PLC Date is: 3/11/2016”
    SCANTIME
      Response: “Current PLC Scan Time is: 561us”
    FIRMWARE
      Response: “Current PLC Firmware is: 176201”
    IPADDRESS
      Response: “Current PLC IP Address is: 10.1.1.200”