## Slide 1: Do-more Technical Training
Communications
(Email)

## Slide 2: Communications – Email
Built-in Ethernet Port
  Supports sending SMTP Email requests to a known SMTP server (MSA/MTA) via the EMAIL instruction
    MUA – Mail User Agent MX – Mail Exchanger
    MSA – Mail Submission Agent MDA – Mail Delivery Agent
    MTA – Mail Transfer Agent
Internet
SMTP
POP / IMAP

## Slide 3: Communications – Email (Connect)
@MyEmailClient (MUA)
Email Server (MSA/MTA)
TCP Protocol
SYN
SYN, ACK
ACK
TCP Connection Established
TCP Connection Established

## Slide 4: Communications – Email (Authorize)
@MyEmailClient (MUA)
Email Server (MSA/MTA)
TCP Connection Established
TCP Connection Established
SMTP Protocol
220 “Ready”
EHLO
250-Hello
250-SIZE
Server tells Client maximum size
250-AUTH LOGIN
Server tells Client what Authorizations are available for use (e.g. LOGIN, PLAIN, CRAM-MD5)
AUTH LOGIN
Client tells Server which Authorization he chooses
334 VXNlcm5hbWU6
Server asks Client for Username using BASE64 encoding
adlxdkej
334 UGFzc3dvcmQ6
Server asks Client for Password using BASE64 encoding
lkujsefxlj
BASE64 Encoding
235 “Successful”
Connection Authenticated
Connection Authenticated

## Slide 5: Communications – Email (Exchange)
@MyEmailClient (MUA)
Email Server (MSA/MTA)
TCP Connection Established
TCP Connection Established
Connection Authenticated
Connection Authenticated
SMTP Protocol
MAIL FROM:<bob>
250-OK
RCPT TO:<alice>
250-OK
DATA
Client tells Server a data stream is to follow
354 “End with .”
Server tells Client to end data stream with a period “.” on a line by itself
“From: <bob>”
[body of email]
Client sends Server all of the email body text (could be several telegrams)
“.”
Client sends Server the period “.” (end of data)
250-OK
QUIT
221-Bye
Email Sent
Email Received

## Slide 6: Communications – Email (Disconnect)
@MyEmailClient (MUA)
Email Server (MSA/MTA)
TCP Connection Established
TCP Connection Established
Connection Authenticated
Connection Authenticated
Email Sent
Email Received
TCP Protocol
FIN, ACK
FIN, ACK
ACK

## Slide 7: Communications – Email
CPU’s Built-in Ethernet Port must have IP address
CPU must have a properly configured SMTP Client Device
  Must know SMTP Server’s (MSA/MTA) IP address or the DNS Lookup name
    Some SMTP Servers have IP addresses that periodically change for security reasons. In this case, the DNSLOOKUP instruction can be used with DEVWRITE instruction to read the IP address dynamically and write it to the CPU’s SMTP Client Device just before doing the EMAIL instruction
  SMTP Server (MSA/MTA) must either use no Authentication (Disabled) or one of the following types:
    AUTH LOGIN
    AUTH PLAIN
    POP before SMTP
  If Authentication is used, the Username & Password must be known for the email account
Must use EMAIL instruction to send

## Slide 8: Communications – Email
CPU’s Built-in Ethernet Port must have IP address:
  Manual config:

## Slide 9: Communications – Email
CPU’s Built-in Ethernet Port must have IP address:
  Programmatic configuration:
    SETUPIP – “Setup TCP/IP Parameters”
    SETUPNOD – “Setup Ethernet Node Parameters”

## Slide 10: Instruction Set (Ethernet)
SETUPIP “Setup TCP/IP Parameters”
  Configures TCP/IP networking parameters for onboard Ethernet port
  Fully asynchronous instruction (red triangle)
  Parameters:
    Ethernet Device: @IntEthernet
    IP Address
      Fixed: Regular IP address format
      Variable: D-memory format (double-word)
    Subnet Mask: (Fixed / Variable)
    Gateway Address: (Fixed / Variable
    On Success: (Set bit / JMP to Stage)
    On Error: (Set bit / JMP to Stage)
  Input leg leading-edge-triggered
  System data words reflect current settings:
    $IPAddress (DST18)
    $NetMask (DST19)
    $Gateway (DST20)
NOTE: Writes to ROM. Could take several seconds to complete. Use sparingly due to ROM’s limited writes (≈100K).
Double-words are used with “unsigned byte” casting to make the line containing the IP address octet in the INIT instruction more readable

## Slide 11: Instruction Set (Ethernet)
SETUPNOD “Setup Ethernet Node Parameters”
  Configures node parameters for onboard Ethernet port
  Fully asynchronous instruction (red triangle)
  Parameters:
    Ethernet Device: @IntEthernet
    Node Number: 32-bit signed (0 to 2,147,483,647)
    Node Name: 0 to 256 alphanumeric characters
      Also stored in system parameter string SysName
    Node Description: 0 to 256 alphanumeric characters
      Also stored in system parameter string SysDesc
    On Success: (Set bit / JMP to Stage)
    On Error: (Set bit / JMP to Stage)
  Input leg leading-edge-triggered
NOTE: Writes to ROM. Could take several seconds to complete. Use sparingly due to ROM’s limited writes (≈100K).

## Slide 12: Communications – Email
Built-in Ethernet Port
  To send Email requires an SMTP Client Device
    Use Device Configuration to create
    Follow Configuration Notes
    DNS Lookup button

## Slide 13: Instruction Set (Ethernet)
PING “Ping Ethernet Device”
  Sends an ICMP ping to see if a particular IP Address is reachable from the Do-more PLC
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device: @IntEthernet
    Remote Address:
      Fixed IP Address
      Variable IP Address – D-memory double-word
      Slave ID – (Module ID)
    Network Timeout: How long to wait in ms (0-65,535)
    Round Trip Time (optional): Time in ms the response took
    On Success: (Set bit / JMP to Stage)
    On Error: (Set bit / JMP to Stage)
  Input leg leading-edge-triggered

## Slide 14: Instruction Set (Ethernet)
EMAIL “Send EMail”
  Sends email
  Fully asynchronous instruction (red triangle)
  Parameters:
    SMTP Device: @MyEmailClient
    To / Cc / Bcc: pertinent email addresses (max 1024 characters)
    Subject: text for the subject line (max 1024 characters)
    Automatically insert space after each term (optional): for use if sending embedded terms in email message
    Message: text body of the email with optional embedded fields (text, control characters, strings, elements, formatting & string selection functions, raw data) – See next slide
    On Success: (Set bit / JMP to Stage)
    On Error: (Set bit / JMP to Stage)
  Input leg leading-edge-triggered

## Slide 15: Instruction Set (Ethernet)
EMAIL “Send EMail”
  Parameters:
    Message: text body of the email
      String Literals – ASCII text in double quotes (e.g. “Hi!”)
      Data Elements – (e.g. “The current count is” CT0.Acc)
      Control Characters
        $$  $
        $”  “
        $L  <LF> (line feed)
        $N  <CR><LF> (carriage return, line feed)
        $P  <FF> (form feed)
        $R  <CR> (carriage return)
        $T  <TAB> (tab)
        $hh  hh (any one-byte hex value)
      Formatting Functions [see Do-more Designer Help Topic DMD0168]
        FmtString – Sets length and/or justifies text within a string
        FmtBit – Formats bits’ values as a text instead of just 0 or 1
        FmtInt – Formats how an integer is represented in a string
        FmtReal – Formats how real numbers are represented in a string
        FmtTMR – Formats how Timer Accumulator values are represented in a string
        FmtDate – Formats how a Date stamp is represented in a string
        FmtTime – Formats how a Time stamp is represented in a string
        Lookup – Selects a string in a list to represent a value
        Raw – Places bytes of data from a data block into a string

## Slide 16: Instruction Set (Ethernet)
DNSLOOKUP “Name to IP Address”
  Finds IP address assigned to a device using DNS protocol.
  Fully asynchronous instruction (red triangle)
  Parameters:
    Device: @IntEthernet
    Preferred DNS Server (Fixed / Variable): IP address to contact for resolving the name. Default is 8.8.8.8 (Google’s public DNS Server)
    Alternate DNS Server (No / Fixed / Variable): IP address to contact if the preferred one fails. Default is the secondary DNS Server IP address from the network setup on the PC running Do-more Designer
    Name: the name that is to be resolved to an IP address (e.g. mail.google.com)
    IP Address Result: where to store the result
    On Success: (Set bit / JMP to Stage)
    On Error: (Set bit / JMP to Stage)
  Input leg leading-edge-triggered

## Slide 17: Instruction Set (Ethernet)
DEVWRITE “Write Device Register”
  Writes a configuration value to a register in a Device
  Parameters:
    Device: @MySMTPClient
    Write Register (pull-down selection): valid registers for chosen Device
    Value: valid value for the register chosen

## Slide 18: Communications – Email
DNSLOOKUP  DEVWRITE  EMAIL
Google’s email server changes IP addresses for security purposes but their domain name doesn’t.
Stage0 uses a DNSLOOKUP instruction to query the DNS server for Gmail’s IP address.
The new IP address is stored in D112, and Stage1 is jumped to
The new IP address is written to the SMTP Client’s IP Address parameter
Stage2 is jumped to
Stage2 sends the email

## Slide 19: Training Station Communication
PLC: 10.1.1.110
EC: 10.1.1.111
PLC: 10.1.1.120
EC: 10.1.1.121
PLC: 10.1.1.130
EC: 10.1.1.131
PLC: 10.1.1.140
EC: 10.1.1.141
PLC: 10.1.1.150
EC: 10.1.1.151
EBC: 10.1.1.112
EBC: 10.1.1.122
EBC: 10.1.1.132
EBC: 10.1.1.142
EBC: 10.1.1.152
Comm PLC: 10.1.1.200
Raspberry Pi: 10.1.1.8
Ethernet Switch
To laptops’ Ethernet Switch
TCP, UDP &
Serial Comms
SNTP, DNS,
Email & DHCP
Serial Comms
SNTP, DNS, Email…
Stepper, encoder, 2 limit switches

## Slide 20: Communications – Email
Email (SNTP) & DNS Server:
  Raspberry Pi  10.1.1.8
Valid emails:
  test0@adcsmiley.tld
  test1@adcsmiley.tld
  test2@adcsmiley.tld
  test3@adcsmiley.tld
  test4@adcsmiley.tld
  test5@adcsmiley.tld
Web Email Client:
  http://adcsmiley.tld
    Login Name: test0, test1, test2, test3, test4, test5
    Password: test