## Slide 1: Do-more Technical Training
Communications
(PEERLINK)

## Slide 2: Communications – PEERLINK
Peerlink communications network
  Data-sharing of 16 blocks of 16 words each
  Uses broadcasts at a rate of 10Hz
  Network can consist of:
    EASY! Do-more PLC w/built-in Ethernet port
      Uses only one PEERLINK instruction in $Main
      Utilizes built-in PL-memory (PL0-255)
    DL-PLC w/ECOM100
      Peerlink configured via ECOM100’s web server (not NetEdit)
      Peerlink blocks mapped to V-memory as configured
    Do-more PLC w/ECOM100 (not recommended)
      Does NOT use PEERLINK instruction
      Peerlink configured via ECOM100’s web server
      Peerlink blocks mapped to DLV-memory as configured
Must turn the ECOM100’s Web Server ON using NetEdit3
Notes: - Use Internet Explorer and log into ECOM100 and show the Peerlink Configuration

## Slide 3: Communications – PEERLINK
Peerlink communications network
  Concepts:
    Publish – analogous to send / write
    Subscribe – analogous to receive / read
    These terms have nothing to do with the PUBLISH & SUBSCRIB instructions
  Blocks (256 unsigned 16-bit words):
    Block0: PL0-15 Block8: PL128-143
    Block1: PL16-31 Block9: PL144-159
    Block2: PL32-47 Block10: PL160-175
    Block3: PL48-63 Block11: PL176-191
    Block4: PL64-79 Block12: PL192-207
    Block5: PL80-95 Block13: PL208-223
    Block6: PL96-111 Block14: PL224-239
    Block7: PL112-127 Block15: PL240-255

## Slide 4: Communications – PEERLINK
Peerlink communications network
  Do-more #1 publishes Block #2
    Do-more #2 hears & puts data in its Block #2
  Do-more #2 publishes Blocks #0 & #1
    Do-more #1 hears & puts data in its Blocks #0 & #1

## Slide 5: Communications – PEERLINK
PEERLINK “Share Data w/PLCs”
  Fully asynchronous (red triangle)
  Parameters:
    Blocks – check which blocks to publish
  Input Leg:
    ON  Publishes at 10 Hz; listens for other blocks
    OFF  No publishing; no listening
  PL: Peerlink Header Structure (next slide)

## Slide 6: Communications – PEERLINK
PEERLINK “Share Data w/PLCs”
  PL: Peerlink Header Structure
    B0Act-B15Act (bit)
      ON: Block publishing or receiving
      OFF:
        Block not published
        Block published; PEERLINK OFF
        Block published; PLC in Program
    Active (word) – 16 Active bits; 1/Block
    B0Err-B15Err (bit)
      ON: Configuration error (>1 device publishing Block)
      OFF: No error
    Error (word) – 16 Error bits; 1/Block
    B0Updated-B15Updated (bit)
      ON: New data for Block this scan
      OFF: No data change since last scan
    Updated (word) – 16 Update bits; 1/Block
    MyBlocks (word) – 16 Publishing bits; 1/Block
    B0Inh-B15Inh (bit)
      ON: prevents updating of Block
      OFF: allows updating of Block
    Inhibit (word) – 16 Inhibit bits; 1/Block
    Enabled (bit) – PEERLINK publishing
    B0Rate-B15Rate (word) – transfers per second

## Slide 7: Communications – PEERLINK
PEERLINK “Share Data w/PLCs”
  Status:
    Offline – input leg OFF
    Subscribe Only – not configured to publish any blocks
    Connecting… - input leg coming ON; gathering data for nodes (1-2 seconds)
    Disconnecting… - input leg going OFF; closing connections (1-2 seconds)

## Slide 8: Communications – PEERLINK
PEERLINK “Share Data w/PLCs”
  Status:
    Green background: normal speed (>7 pkts/sec). Blocks 0, 1, 3, 5, 6 & 15
    Yellow background: slow speed (4-7 pkts/sec). Block 2
    Red background: very slow speed (<3 pkts/sec). Block 4
    No highlight & grayed #: no packets publishing to this Block. Blocks 7, 9, 10, 11, 12, 13 & 14
    Bold box outline: Blocks published by this PEERLINK instruction. Block 0
    Any highlight w/Grayed #: updates to this block are inhibited. Blocks 3 & 5
      PEERLINK publishing the Block, Inhibit prevents publishing of that Block
      PEERLINK listening to Block, Inhibit prevents that Block from being updated
    Red Circle w/Slash: more than one device on the Peerlink network is publishing to this block (configuration error). Block 8

## Slide 9: Communications – PEERLINK
Do-more CPU
PEERLINK
UDP
Peerlink Device
Do-more CPU
PL0-255
Peerlink Device
Peerlink Publishing
Peerlink Subscribing
PL0-255
PEERLINK
Do-more CPU
PEERLINK
UDP
Peerlink Device
Peerlink Publishing
PL0-255
Do-more CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
@ECOM_001
DLV
Do-more CPU
PEERLINK
UDP
Peerlink Device
Peerlink Publishing
PL0-255
DL-CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
V-memory
In this case a PEERLINK instruction is not necessary because the ECOM100 is subscribing and writing to “V” (i.e. DLV)

## Slide 10: Communications – PEERLINK
UDP
Do-more CPU
PL0-255
Peerlink Device
Peerlink Subscribing
PEERLINK
UDP
Do-more CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
@ECOM_001
DLV
Do-more CPU
Peerlink Publishing
E
C
O
M
1
0
0
Peerlink Config
@ECOM_001
DLV
Do-more CPU
E
C
O
M
1
0
0
Peerlink Config
DL Server
DLV
Peerlink Publishing
DL-CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
V-memory
UDP
Do-more CPU
E
C
O
M
1
0
0
Peerlink Config
DL Server
DLV
Peerlink Publishing
In all these cases a PEERLINK instruction is not necessary for publishing because the ECOM100 is doing that itself
In this case a PEERLINK instruction is not necessary because the ECOM100 is subscribing and writing to “V” (i.e. DLV)

## Slide 11: Communications – PEERLINK
UDP
Do-more CPU
PL0-255
Peerlink Device
Peerlink Subscribing
PEERLINK
UDP
Do-more CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
@ECOM_001
DLV
Peerlink Publishing
DL-CPU
Peerlink Subscribing
E
C
O
M
1
0
0
Peerlink Config
V-memory
UDP
DL-CPU
E
C
O
M
1
0
0
Peerlink Config
V-memory
Peerlink Publishing
DL-CPU
E
C
O
M
1
0
0
Peerlink Config
V-memory
Peerlink Publishing
DL-CPU
E
C
O
M
1
0
0
Peerlink Config
V-memory
In this case a PEERLINK instruction is not necessary because the ECOM100 is subscribing and writing to “V” (i.e. DLV)

## Slide 12: Communications – PEERLINK
# | Publishing or Subscribing CPU | Ethernet Port | Instruction | Device | Memory
1 | Do-more | Internal | PEERLINK | @IntEthernet | PL0-255
2 |  | ECOM100 (Peerlink Config) | None | @ECOM_001 | DLV
3 | DL-PLC |  |  | n/a | V

## Slide 13: Communications – PEERLINK
Write a changing value to your PL
Block0 PL0
Block1 PL16
Block2 PL32
Block3 PL48
Block4 PL64