## Slide 1: Do-more Technical Training
Communication
(Time Sync)

## Slide 2: Communication (Time Sync)
CPU Configuration
  TimeSync Configuration
Notes: Launchpad: nothing new here
Project Browser:
  Buttons
    Control Logic Filter – Display filter
    New Code Block – Create new code blocks
    Execution Order – Change execution order of blocks
    Status – Shows which blocks are enabled to run
    Sort Code Blocks – Change display order
    Sort Memory – Change display order
  Control Logic
  Configuration
  Tools
Debug View
  NOTE: Message Dump – enables dump to Do-more Logger, $EnableMsgDump (ST36)
Data View
PID Overview

## Slide 3: Communication (Time Sync)
TimeSync Configuration
  Automatic time sync network
    1 server
    1 or more alternate server(s)
    1 or more client(s)
  TCP/IP broadcast (network domain)
  Disabled: default
  Client:
    Listens for server’s time-sync packet
    If heard 
      $TimeSynced (ST23) = ON
      Sets real-time clock
      Keeps listening (times down from Update Interval)
    If Update Interval times out 
      $TimeSynced (ST23) = OFF
      Keeps listening (times down from Update Interval)
  Server: transmits 3 time-sync packets (5 second intervals) every Update Interval)
  Alternate:
    Normally a Client
    If Update Interval times out + 15 seconds 
      Becomes the new Server
  Update Interval: 0 – 32,767 minutes (22 days)
Notes: Launchpad: nothing new here
Project Browser:
  Buttons
    Control Logic Filter – Display filter
    New Code Block – Create new code blocks
    Execution Order – Change execution order of blocks
    Status – Shows which blocks are enabled to run
    Sort Code Blocks – Change display order
    Sort Memory – Change display order
  Control Logic
  Configuration
  Tools
Debug View
  NOTE: Message Dump – enables dump to Do-more Logger, $EnableMsgDump (ST36)
Data View
PID Overview

## Slide 4: Onboard Clock
Automatic Setting:
  NETTIME “SNTP Client” instruction
    Retrieves date/time from an SNTP (Simple Network Time Protocol) Server & stored in $UTC (DST21)
    Parameters:
      Device – onboard Ethernet port
      SNTP Server IP Address
        Fixed IP Address – IP address of SNTP Server
        Variable IP Address – (32-bit word) variable IP address of SNTP Server commonly obtained by DNSLOOKUP “Name to IP Address” instruction
      UDP Port Number – SNTP Protocol default is 123
      Network Timeout – 1 to 65.535 seconds
      On Success, On Error – Action to take
    Instruction is leading-edge triggered
    NOTE: NTP protocol is not supported
Notes: * Program NETTIME using Richard’s SNTP server IP address (10.1.1.8)

## Slide 5: Communication (Time Sync)
Server
Alt
Client 1
Client 2
Client 3
1 Server
1 Alternate Server
TimeSync
Broadcast
Update
Time
15-Feb-2016
2:01:01 PM
$TimeSynced = OFF
15-Feb-2016
2:01:15 PM
$TimeSynced = OFF
15-Feb-2016
2:01:20 PM
$TimeSynced = OFF
15-Feb-2016
2:01:21 PM
$TimeSynced = OFF
15-Feb-2016
2:01:23 PM
15-Feb-2016
2:01:23 PM
$TimeSynced = ON
15-Feb-2016
2:01:23 PM
$TimeSynced = ON
15-Feb-2016
2:01:23 PM
$TimeSynced = ON
15-Feb-2016
2:01:23 PM
$TimeSynced = ON
Repeats 2 more times at 5-sec intervals
Server drops offline for some reason
15-Feb-2016
2:02:23 PM
$TimeSynced = OFF
15-Feb-2016
2:02:23 PM
$TimeSynced = OFF
15-Feb-2016
2:02:23 PM
$TimeSynced = OFF
15-Feb-2016
2:02:23 PM
$TimeSynced = OFF
Update Interval timesout (60 seconds)
Update Interval timesout (60 seconds)
Update Interval timesout (60 seconds)
Update Interval timesout (60 seconds)
15-Feb-2016
2:02:38 PM
$TimeSynced = OFF
15-Feb-2016
2:02:38 PM
$TimeSynced = OFF
15-Feb-2016
2:02:38 PM
$TimeSynced = OFF
15-Feb-2016
2:02:38 PM
$TimeSynced = OFF
15 seconds more pass
15-Feb-2016
2:02:38 PM
TimeSync
Broadcast
Update
Time
15-Feb-2016
2:02:38 PM
$TimeSynced = ON
15-Feb-2016
2:02:38 PM
$TimeSynced = ON
15-Feb-2016
2:02:38 PM
$TimeSynced = ON
Repeats 2 more times at 5-sec intervals
Notes: Launchpad: nothing new here
Project Browser:
  Buttons
    Control Logic Filter – Display filter
    New Code Block – Create new code blocks
    Execution Order – Change execution order of blocks
    Status – Shows which blocks are enabled to run
    Sort Code Blocks – Change display order
    Sort Memory – Change display order
  Control Logic
  Configuration
  Tools
Debug View
  NOTE: Message Dump – enables dump to Do-more Logger, $EnableMsgDump (ST36)
Data View
PID Overview