## Slide 1: Do-more Technical Training
Designer Basics

## Slide 2: Programming Environment
Toolbar
Utilities
Tabs
Status

## Slide 3: Programming Environment
Toolbars
  Offline
  Online
  Ladder
  File
  Edit
  Search
  View
  Tools
  PLC
  Debug
  Window
  Help

## Slide 4: Programming Environment
Utilities
  Launchpad
  Project Browser
  Debug View
  Data View
  PID Overview

## Slide 5: Programming Environment
Utilities
  Launchpad
    Projects
    Applications
    Links

## Slide 6: Programming Environment
Utilities
  Launchpad
    Projects
      Remove – Removes project from list and/or from disk
      Folders – Change project folder locations

## Slide 7: Programming Environment
Utilities
  Launchpad
    Applications
Do-more Designer
Do-more Logger

## Slide 8: Programming Environment
Utilities
  Launchpad
    Applications
Do-more Designer
Do-more Logger
  Displays debug & status messages received from Do-more CPU w/ Ethernet port.
  Packets are sent to UDP Port # 7272(hex)
  $EnableMsgDump (ST36) = ON to enable
  Very handy for troubleshooting EMAIL

## Slide 9: Programming Environment
Utilities
  Launchpad
    Applications
Do-more Designer
Do-more Logger
NetEdit3
IPConfig
  Recover missing Ethernet device (NetEdit can’t see; IPX unavail)
  (1) Select Adapter at bottom
  (2) Get MAC address from device’s label
  (3) Enter MAC address in “Ethernet Address”
  (4) Enter “IP Address” you want missing device to have (must be on PC’s subnet)
  (5) “Subnet Mask” got set when Adapter was selected (but you can change it)
  (6) Press <Write> button  “Cool! Found device!” or “Sorry! Unable to find device!”

## Slide 10: Programming Environment
Utilities
  Launchpad
    Applications
Do-more Designer
Do-more Logger
NetEdit3
IPConfig
Do-more Version
DmDesigner1_3.ini
DMLoader
DBWin32Logger
ERM Workbench
205 Do-more Hardware Manual
Terminator Do-more Manual
Visit AutomationDirect
Visit Host Engineering
Host Forum, FAQs, Downloads…
Calculator
Windows Network Control Panel
Windows Firewall
Windows Device Manager
Windows Services
CTRIO WB 2 – Do-more PLC
CTRIO WB 2 – DirectcLogic PLC
CTRIO WB 2 – Offline

## Slide 11: Programming Environment
Utilities
  Project Browser
    Control Logic
    Configuration
- Control Logic Filter
- New Code Block
- Execution Order
- Status
- Sort Code Blocks
- Sort Memory

## Slide 12: Programming Environment
Utilities
  Project Browser
    BUTTONS
- Execution Order
- Status

## Slide 13: Programming Environment
Utilities
  Project Browser
    Control Logic
      Shows all Programs & Tasks
      Programs expand to show Rungs & Stages
      Tasks expand to show Rungs
      Shows first line of Comment
      Double-click opens code block in Ladder View
      When in Edit Mode, right-click on code block allows many functions (e.g. create, remove, etc.)

## Slide 14: Programming Environment
Utilities
  Project Browser
    Configuration: lists Data Blocks, Heap Items & Devices
      Memory – all memory types in System Configuration
      Devices – all system-created & user-created Devices in System Configuration, e.g.
        @CTRIO_001_C1F1
        @IntEthernet
        @IntModTCPClient
      Unassigned Nicknames – any Nicknames not yet assigned to actual memory
Notes: Have them open the Memory section
Do System Configuration and configure the internal serial port to “General Purpose”
Enter a STREAMIN (with Network Timeout set to 10 seconds)
Enable STREAMIN (pull up the Device Status) to show the hotlink

## Slide 15: Programming Environment
Utilities
  Debug View
    Debug – enable
    Pause – stops scan
    Scan – starts scan
    Single Scan – runs one scan then pauses
    N-Scan – runs # of scans then pauses
    Stages – enable/disable
    Message Dump – enable to Do-more Logger app; sets $EnableMsgDump (ST36) = ON
    Watchdog… - test hardware or software watchdog
    Unsuspend, Unsuspend All, Suspend… - manually for Program or Task
Notes: Enter INC D0
Put D0 in Data View to watch it increment
Put $EnableDebug (ST33) in Data View
Pull up Debug  Debug View
Notice you can turn ST33 ON or OFF in Data View or in Debug View
Turn it ON
<Pause> … D0 stops incrementing
<Scan> … D0 increments again
<Pause> … D0 stops incrementing
<Single Scan> … D0 increments once
Enter 10 into the N-scan variable
<N-scan> … D0 increments 10 times
Create MyTask task
  Program INC D1
Back in $Main, enter C0 to ENTASK “MyTask” (power flow, not edge)
C0 = ON … D1 increments
Debug mode
<Pause> … D0 & D1 stop incrementing
<Single Scan> … D0 & D1 increment by 1
<Scan> … D0 & D1 incrementing
<Suspend…> MyTask … D1 stops incrementing (D0 keeps incrementing), MyTask is listed as suspended
In Project Browser, MyTask (with status ON) shows yellow
Select MyTask in Debug View, <Unsuspend> … D0 & D1 both incrementing
Exit Debug

## Slide 16: Programming Environment
Utilities
  Data View
    Right-click

## Slide 17: Programming Environment
Utilities
  PID Overview

## Slide 18: Programming Environment
Tabs
  Top
    Start Page
    Ladder Views
    Trend Views
    PID Views
    Documentation Editor
  Bottom (dock/float)
    Cross Reference View
    Output Window

## Slide 19: Programming Environment
Tabs
  Top
    Start Page (Global)
      Customizable

## Slide 20: Programming Environment
Tabs
  Top
    Ladder View
      Individual tabs
      Re-orderable tabs
      Scroll (arrows/wheel)
      Search  Find (CTRL-F)
      Search  Goto (CTRL-G)
      View  Options  Ladder
      Hover Element (Xref w/links)
      Hover Instruction (Help w/links)
      View  Themes…
      View  Color Setup…
      Split screen bar
      Window  New Window, Cascade, Tile Horizontally, Tile Vertically, Arrange Icons
      Window  Default Layout (Recover!)
      View  Zoom In / Zoom Out (buttons / toolbar)

## Slide 21: Programming Environment
Tabs
  Top
    Ladder View
      Status bar
        Project Differences (hover)
          S = System Configuration
          P = Program
          D = Documentation
          Colors
            Green: not saved to disk
            Cyan: not saved to PLC
        Program Usage
          Used / Available
          Click for System Information
        Cursor Location
          <CodeBlock>#<Rung>:<Row>:<Column>

## Slide 22: Programming Environment
Tabs
  Top
    Trend View
      Logging / Historical
      Panes:
        Discrete
        Integers / Real
      Crosshair cursor
        Click for snapshot
      Zoom: CTRL + wheel
      Buttons:
        Opt – Trend View Options
        Hist – Toggle historical mode
        Exp – Export range of data points
        Sync – Synchronize time
        Rec – Record data to a file
        Pse – Pause recording
      Time Scale slider (500ms to 1 hour)
Notes: Have them program a RAMPSOAK and use a system toggle bit (i.e. ST4 ($1second))
Pull up Data View with pertinent parameters
Right-click on Data View and select Trend All
Play with various things in Trend View

## Slide 23: Programming Environment
Tabs
  Top
    PID View
      Configuration, tuning & monitoring
      3 panes
        Data form
        PV / SP trend
        Output / Bias trend

## Slide 24: Programming Environment
Tabs
  Top
    Documentation Editor
      Saved in the PLC
      PLC  System Information  Memory Usage box shows Max Documentation & Documentation Used
      Displays only used
      Element: program element
        (*) no documentation
      Nickname: 16 characters
      Extra Info: 16 characters
      Description: 132 characters
        CTRL-Enter manual line break
      Buttons:
        Add Record
        Add Sym Const – e.g. PI = 3.14159
        Clean Database – remove records not being used
        Find
        Find Again

## Slide 25: Programming Environment
Tabs
  Bottom
    Dockable / Floatable
      Cross Reference View
        Tools  Cross Reference… or CTRL-Y
        Modes:
          (1) Xref mode
          (2) Usage mode

## Slide 26: Programming Environment
Tabs
  Bottom
    Dockable / Floatable
      Cross Reference View
        Modes:
          (1) Xref mode
            Element
            Extended Info – Structure member / Casting
            Access Type – Input, Output, In/Out
            Address - <CodeBlock>@<Address>
            Instruction
            Parameter Info – Instruction’s parameter
            Double-click places cursor

## Slide 27: Programming Environment
Tabs
  Bottom
    Dockable / Floatable
      Cross Reference View
        Modes:
          (1) Xref mode
            Buttons
              Follow Ladder Cursor
              Point Scope – Ladder View cursor itself
              Instruction Scope – Ladder View instruction
              Rung Scope – Ladder View rung
              Block Scope – Ladder View code block
              Full Scope – Entire project
              Include Bits
              Include Numerics
              Include Structures
              Include Devices
              Include Inputs
              Include Outputs
              Expand – include range entries (e.g. SETR “C100 thru C120”)
              Sort order – Element, Nickname, Data-Block/Number ID

## Slide 28: Programming Environment
Tabs
  Bottom
    Dockable / Floatable
      Cross Reference View
        Modes:
          (2) Usage mode
            Buttons
              Follow Ladder Cursor
              Reverse Usage
              Field Size 8
              Field Size 10
              Field Size 16
            X = explicit use
            [ = start range
            ] = end range
            – = inside range

## Slide 29: Programming Environment
Tabs
  Bottom
    Dockable / Floatable
      Output Window
        Displays errors, warnings & info
        Can be activated by:
          Edit  Accept
          PLC  Program Check
          File  Import
          Search  Replace…
          Changes to System Configuration
          After PID Auto-tune
          Connecting to PLC
        Filter Buttons: Error, Warning, Message

## Slide 30: Programming Environment
Status Bar
FUNCTION | POSSIBLE VALUES | APPEARANCE
Writing to PLC | N/A | 
PLC writing ROM | N/A | 
PLC Mode Switch | Run, Term, Stop | 
Force status | Forces, Forces Suspended | 
Project/PLC sync | System (S), Program (P), Documentation (D) | 
Device status | Devs OK, Device Error | 
PLC status | PLC OK, Info, Warning, Error | 
Session status | Online-Offline/<user>/<link> | 
PLC mode | Run, Program | 
Memory usage | Program: <current>/<total> | 
PLC type | e.g. H2-DM1E | 
Cursor position | <CodeBlock>#<Rung>:<Row>:<Column> |