## Slide 1: Do-more Technical Training
The Do-more Way

## Slide 2: Do-more Architecture
Hardware or System Resource
Device
Memory
Instruction
Server
Do-more PLCs are “device-centric”
Devices interface directly to the PLC’s hardware & system resources, handling low-level issues like protocols, handshaking, memory allocation, status flags & communication buffer management
Devices provide a uniform interface to the hardware for the instructions
Devices also provide a uniform interface to the hardware for the memory
Most instructions do not use Devices but interface directly to memory
Servers are similar to Devices but run in the background
Servers (like Devices) interface directly to the PLC’s hardware or System Resources
Servers (like Devices) also provide a uniform interface to the hardware for the memory
With a few exceptions, Servers do not normally interface with instructions
Devices are interfaces that provide access to Do-more resources

## Slide 3: Advantages of Device-Centricism
Provides a level of abstraction
  Reduces complexity when interfacing to the PLC’s system resources (e.g. hardware)
  Increases efficiency in handling complex functions
Provides a uniform programming interface even if the hardware is different
Provides a uniform interface to memory so it is impossible to have memory mapping issues
Provides clearly-named memory structures that give access to the particular device’s features & functions
Handles the hardware asynchronously for the programmer
Think of the standard interfaces to a computer (mouse, keyboard, monitor), or a phone (touch screen, swipe, long press), etc. These interfaces are generic even though providing access to very different hardware.

## Slide 4: Do-more Devices
Three types:
  (1) Built-in(1) – exist by default
    @DMLogger
    @IntEIPClient
    @IntEthDMPPClient
    @IntEthernet
    @IntModTCPClient
    @IntSerial
    @LocalIOMaster
    @UserLog
  (2) System-created – created by system as user modifies CPU Configuration or adds modules to system
    @IntSerModbusClient(1)
    @IntEIPServer(1)
    @EthIOMaster(1)
    @CTRIO_xxx(2)
    @CTRIO_xxx_CyFz(2)
    @CTRIO_xxx_Outy(2)
    @ECOM_xxx(2)
    @ERM(2)
    @GSEDRV100(2)
    @SERIO_xxx_y(2)
  (3) User-created – created manually by the user(2)
    @EtherNetIPClient
    @ModbusTCPClient
    @SMTPClient
    @TCPClient
    @TCPServer
    @UDPConnection
    (1) Name of Device(s) cannot be changed
    (2) Name given upon creation (changeable)

## Slide 5: Do-more Configuration Hierarchy
CPU Configuration
I/O Configuration
Module Configuration(s)
Device Configuration
I/O Mappings
Memory Configuration
The order is on purpose!
The order is on purpose!

## Slide 6: (1) CPU Configuration Ethernet Port: Can handle many simultaneous Devices/Servers/Functions
Ethernet Port
DomoreServer
DLServer
@IntEthernet
Peerlink
Function
2ndInt EthServer
ModbusTCP Server
Ethernet IP Server
@EthIOMaster
@SMTPClient
@TCPClient

## Slide 7: (1) CPU Configuration Serial Port: Only does one Configuration
Serial Port
@IntSerial
Do-more Programming Configuration:
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
K-Sequence Server Configuration:
Station
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
Modbus RTU Server (Slave) Configuration:
Unit ID
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
Modbus RTU Client (Master) Configuration:
Timeout
Retries
Inter-packet Delay
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
General Purpose Configuration:
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control

## Slide 8: (1) CPU Configuration (Default)
Uses Internal Ethernet Port
The following are not manually configurable
All use the @IntEthernet Device
  Do-more Server
    Allows access to all Do-more memory
    Do-more Designer uses this
  DL Server
    Allows access to DL-memory
  SNTP “Simple Network Time Protocol”
    Used by NETTIME instruction to set CPU time
  ICMP “Internet Control Message Protocol”
    Responds to external “pings”
    Used by PING instruction to find an IP address
  DNS “Domain Name System” Protocol
    Used by DNSLOOKUP instruction to find IP address
  Peerlink Function
    Used by PEERLINK instruction for easy comms
    Allows access to PL-memory blocks (16 blocks of 16 words)
    Allows access to PL memory structure

## Slide 9: Do-more Architecture (1) CPU Configuration – Do-more Server
Internal Ethernet Port
All PLC Memory
Do-more Server on @IntEthernet
Do-more Server runs in the background
Do-more Server interfaces directly to the Internal Ethernet Port
Do-more Server provides a uniform interface to the hardware for all the PLC’s memory

## Slide 10: Do-more Architecture (1) CPU Configuration – DL Server (K-seq)
Internal Ethernet Port
DL-Memory
DL Server on @IntEthernet
DL Server runs in the background
DL Server interfaces directly to the Internal Ethernet Port
DL Server provides a uniform interface to the hardware for DL memory

## Slide 11: Do-more Architecture (1) CPU Configuration – SNTP “Simple Network Time Protocol”
Internal Ethernet Port
@IntEthernet
Do-more Memory
NETTIME
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the SNTP “Simple Network Time Protocol”
@IntEthernet Device provides interface to the hardware for the NETTIME instruction
NETTIME instruction uses Do-more memory for parameters
@IntEthernet Device provides access to Internal Ethernet Port

## Slide 12: Do-more Architecture (1) CPU Configuration – ICMP “Internet Control Message Protocol”
Internal Ethernet Port
@IntEthernet
Do-more Memory
PING
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the ICMP “Internet Control Message Protocol” & responding to external ICMP “pings”
@IntEthernet Device provides interface to the hardware for the PING instruction
PING instruction uses Do-more memory for parameters

## Slide 13: Do-more Architecture (1) CPU Configuration – DNS “Domain Name System” Protocol
Internal Ethernet Port
@IntEthernet
Do-more Memory
DNSLOOKUP
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the DNS “Domain Name System” protocol
@IntEthernet Device provides interface to the hardware for the DNSLOOKUP instruction
DNSLOOKUP instruction uses Do-more memory for parameters

## Slide 14: Do-more Architecture (1) CPU Configuration – Peerlink Function
Internal Ethernet Port
@IntEthernet
PL Blocks PL Structure
PEERLINK
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the Peerlink Protocol
@IntEthernet Device provides interface to the hardware for the PEERLINK instruction
@IntEthernet Device provides a uniform interface to the hardware for PL Memory

## Slide 15: (1) CPU Configuration (Manual)
TimeSync Configuration (@IntEthernet)
  Allows access to:
    SDT0 ($Now) system date/time structure
    ST23 ($TimeSynced) system bit
Internal Ethernet Port (@IntEthernet)
  Configure IP settings
  Enable Secondary Ethernet Connection
    Allows access to all Do-more memory over a different UDP Port Number
    Do-more Designer uses this
  (By default, DLRX/DLWX instructions can be used)
Modbus/TCP Server Configuration (@ModbusTCPServer)
  Allows access to M-memory
  Uses ModbusTCPServer memory structure
Ethernet/IP Explicit Message Server (@IntEIPServer)
  Allows access to up to 8 configured Do-more memory blocks
  Uses $IntEIPServer memory structure

## Slide 16: Do-more Architecture (1) CPU Configuration – TimeSync Configuration
Internal Ethernet Port
@IntEthernet
SDT0 ($Now) ST23 ($TimeSynced)
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the Time Sync Protocol
@IntEthernet Device provides a uniform interface to the hardware for System Clock Memory
TimeSync Configuration:
Client
Server
Alternate
Update Interval

## Slide 17: Do-more Architecture (1) CPU Configuration – IP Configuration
Internal Ethernet Port
@IntEthernet
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling all Ethernet telegrams
IP Configuration:
Module ID
Name
Description
IP Address
Subnet Mask
Gateway

## Slide 18: Do-more Architecture (1) CPU Configuration – Secondary Ethernet Connection
Internal Ethernet Port
All PLC Memory
Do-more Server on @IntEthernet
Do-more Server runs in the background
Do-more Server interfaces directly to the Internal Ethernet Port
Do-more Server provides a uniform interface to the hardware for all the PLC’s memory
Secondary Ethernet Connection:
Enable
UDP Port Number

## Slide 19: Do-more Architecture (1) CPU Configuration – DL Client (K-seq)
Internal Ethernet Port
@IntEthernet
Do-more Memory
DLRX
DLWX
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the hidden background DL Client’s K-seq protocol
@IntEthernet Device provides interface to the hardware for the DLRX/DLWX instructions
DLRX/DLWX instructions use Do-more memory for parameters

## Slide 20: Do-more Architecture (1) CPU Configuration – Modbus TCP Server (Slave)
Internal Ethernet Port
M-Memory
$ModbusTCPServer
@ModbusTCPServer
ModbusTCP Server runs in the background but is visible & configurable
Modbus TCP Server interfaces directly to the Internal Ethernet Port
Modbus TCP Server provides a uniform interface to the hardware for M-memory & the Server’s Structure
Modbus TCP Server Configuration:
Enable
Maximum Concurrent Sessions
Client Inactivity Timeout
TCP Port Number

## Slide 21: Do-more Architecture (1) CPU Configuration – EtherNet/IP Explicit Message Server
Internal Ethernet Port
Block1-8
$IntEIPServer
@IntEIPServer
EtherNet/IP Explicit Message Server runs in the background but is visible & configurable
EtherNet/IP Explicit Message Server interfaces directly to the Internal Ethernet Port
EtherNet/IP Explicit Message Server provides a uniform interface to the hardware for Block1-8 & the Server’s Structure
EtherNet/IP Explicit Message Server Configuration:
Enable
Maximum Concurrent Sessions
Client Inactivity Timeout
TCP Port Number
Device Name
Block1-8

## Slide 22: (1) CPU Configuration (Manual)
Serial Port Mode (@IntSerial)
  Do-more Programming
    Allows access to all Do-more memory
    Uses $IntSerialServer memory structure
  K-sequence Server
    Allows access to DL-memory
    Uses $IntSerialServer memory structure
  Modbus RTU Server (Slave)
    Allows access to M-memory
    Uses $IntSerialServer memory structure
  Modbus RTU Client (Master) (@IntSerModbusClient)
    Used by MRX/MWX instructions
  General Purpose
    Used by STREAMIN/STREAMOUT instructions
    Uses $IntSerial memory structure
Default Watchdog Timeout
  Uses:
    ST13 ($WatchdogReboot) system bit
    ST24 ($HwWatchdogMode) system bit
    ST25 ($DisableHwWdog) system bit
    ST37 ($DisableSwWdog) system bit
    ST128 ($WatchdogTimeout) system bit
    DST23 ($WatchdogTimeVal) system double word
    DST385 ($WatchdogReboots) system double word
  Used by WATCHDOG instruction

## Slide 23: Do-more Architecture (1) CPU Configuration – Do-more Programming
Internal Serial Port
All PLC Memory
$IntSerialServer
Do-more Server on @IntSerial
Do-more Server runs in the background
Do-more Server interfaces directly to the Internal Serial Port
Do-more Server provides a uniform interface to the hardware for all the PLC’s memory
Serial Port Settings:
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control

## Slide 24: Do-more Architecture (1) CPU Configuration – DL Server (K-seq)
Internal Serial Port
DL-Memory
$IntSerialServer
DL Server on @IntSerial
DL Server runs in the background
DL Server interfaces directly to the Internal Serial Port
DL Server provides a uniform interface to the hardware for DL memory & $IntSerialServer
Serial Port Settings:
Station
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control

## Slide 25: Do-more Architecture (1) CPU Configuration – Modbus RTU Server (Slave)
Internal Serial Port
M-Memory
$IntSerialServer
Modbus RTU Server on @IntSerial
Modbus RTU Server runs in the background but is visible & configurable
Modbus RTU Server interfaces directly to the Internal Serial Port
Modbus RTU Server provides a uniform interface to the hardware for M-memory & the Server’s Structure
Modbus RTU Server Settings:
Unit ID
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control

## Slide 26: Do-more Architecture (1) CPU Configuration – Modbus RTU Client (Master)
Internal Serial Port
@IntSerModbusClient
Do-more Memory
MRX
MWX
@IntSerModbusClient Device interfaces directly to the Internal Serial Port handling the Modbus RTU protocol
@IntSerModbusClient Device provides interface to the hardware for the MRX/MWX instructions
Modbus RTU Client Configuration:
Timeout
Retries
Inter-packet Delay
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
MRX/MWX instructions use Do-more memory for parameters

## Slide 27: Do-more Architecture (1) CPU Configuration – General Purpose
Internal Serial Port
@IntSerial
Do-more Memory
IntSerial Structure
STREAMIN
STREAMOUT
@IntSerial Device interfaces directly to the Internal Serial Port handling the general purpose comms
@IntSerial Device provides interface to the hardware for the STREAMIN/STREAMOUT instructions
Serial Port Settings:
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
STREAMIN/STREAMOUT instructions use Do-more memory for parameters
@IntSerial Device provides a uniform interface to the hardware for the IntSerial Structure

## Slide 28: Do-more Architecture (1) CPU Configuration – Watchdog Function
Do-more CPU
Watchdog-related System Memory
(e.g. ST128, DST23)
Watchdog Function
Watchdog Function runs in the background but is configurable
Watchdog Function interfaces directly to the Do-more CPU
Watchdog Function provides a uniform interface to the hardware for Watchdog-related System memory
Default Watchdog Settings:
Default Timeout
WATCHDOG
Watchdog Function provides a uniform interface for the WATCHDOG instruction

## Slide 29: (2) I/O Configuration
DL205 Local Master (@LocalIOMaster)
  Allows Auto/Manual Configuration of I/O
  Allows access to I/O memory
  Uses LocalIOMaster memory structure
Ethernet I/O Master (@EthIOMaster)
  Controls up to 16 EBC100 slaves
  Allows access to I/O memory
  Uses $EthIOMaster memory structure

## Slide 30: Do-more Architecture (2) I/O Configuration – Local I/O Master
Backplane w/Modules
@LocalIOMaster
I/O Memory
Do-more Memory
LocalIOMaster Structure
Smart-Module Instructions
@LocalIOMaster Device interfaces directly to the Backplane handling the module communications
@LocalIOMaster Device provides interface to the hardware for smart-module Devices & their instructions
Local I/O Master Configuration:
Auto
Manual
Instructions use Do-more & I/O memory for parameters
@LocalIOMaster Device provides a uniform interface to the hardware for the I/O memory & LocalIOMaster Structure

## Slide 31: Do-more Architecture (2) I/O Configuration – Ethernet I/O Master
Internal Ethernet Port
@EthIOMaster
I/O Memory
Do-more Memory
$EthIOMaster
Instructions
@EthIOMaster Device interfaces directly to the Internal Ethernet port handling the EBC100 Slave module communications
Ethernet I/O Master Configuration:
EBC100 Slaves & their I/O Configurations
Instructions use Do-more & I/O memory for parameters
@EthIOMaster Device provides a uniform interface to the hardware for the I/O memory & $EthIOMaster Structure

## Slide 32: (3) Module Configuration
CTRIO/CTRIO2 (@CTRIO_001)
  Creates @CTRIO_001 device that uses $CTRIO_001 memory structure
  Creates various memory structures as module is configured (e.g. $CTRIO_001_C1F1)
  Used by all CTxxxxxx & RD/WT instructions
ECOM/ECOM100 (@ECOM_002)
  Allows access to DL-memory
  Can be used by DLRX/DLWX & RD/WT instructions
ERM/ERM100 (e.g. @ERM_003)
  Allows access to Do-more memory or DL-memory
  Can be used by DLRX & RD/WT instructions
F2-8AD4DA-x
  Allows configuration of resolution, track & hold, input/output ranges
GS Drive (e.g. @MyGSDrive)
  Uses $MyGSDrive memory structure
  Used by GSREGRD/GSREGWR instructions

## Slide 33: Do-more Architecture (3) Module Configuration – CTRIO2 Module
CTRIO2 Module
@CTRIO_001
$CTRIO_001
Do-more Memory
CTREGRD
CTREGWR
@CTRIO_001 Device interfaces directly to the CTRIO2 via the I/O Master handling the CTRIO2 module communications
@CTRIO_001 Device provides interface to the hardware for the CTREGRD & CTREGWR instructions
Instructions use Do-more memory for parameters
@CTRIO_001 Device provides a uniform interface to the hardware for the $CTRIO_001 Structure
The @CTRIO_001 Device is automatically created when a CTRIO2 module is plugged into an I/O Master’s base

## Slide 34: Do-more Architecture (3) Module Configuration – CTRIO Input Functions
CTRIO2 Input Functions
@CTRIO_001_C1F1
$CTRIO_001_C1F1
Do-more Memory
Instructions
@CTRIO_001_C1F1 Device interfaces directly to the CTRIO2 via the I/O Master handling the CTRIO2 module communications for input functions (counter, timer, pulse catch)
Instructions use Do-more memory for parameters
@CTRIO_001_C1F1 Device provides a uniform interface to the hardware for the $CTRIO_001_C1F1 Structure
The @CTRIO_001_C1F1 Device is automatically created if the CTRIO2 module is configured with an Input Function

## Slide 35: Do-more Architecture (3) Module Configuration – CTRIO Output Functions
CTRIO2 Output Functions
@CTRIO_001_Out2
$CTRIO_001_Out2
Do-more Memory
CTRIO Instructions
@CTRIO_001_Out2 Device interfaces directly to the CTRIO2 via the I/O Master handling the CTRIO2 module communications for output functions (raw output, discrete output, pulse output)
@CTRIO_001_Out2 Device provides interface to the output functions of the CTRIO2 for all the CTRIO instructions
Instructions use Do-more memory for parameters
@CTRIO_001_Out2 Device provides a uniform interface to the hardware for the $CTRIO_001_Out2 Structure
The @CTRIO_001_Out2 Device is automatically created if the CTRIO2 module is configured with an Output Function

## Slide 36: Do-more Architecture (3) Module Configuration – ECOM100 Module
ECOM100 Module
@ECOM_001
DL-Memory
Do-more Memory
DLRX
DLWX
@ECOM_001 Device interfaces directly to the ECOM100 via the @LocalIOMaster handling the ECOM100 module communications
@ECOM_001 Device provides interface to the ECOM100 for the DLRX/DLWX instructions
DLRX/DLWX use Do-more memory for parameters
@ECOM_001 Device provides a uniform interface to the ECOM100 for DL-Memory
Must use NetEdit3 to Configure:
IP network parameters
Peer-to-peer table
Email, etc.
The @ECOM_001 Device is automatically created when an ECOM100 module is plugged into an I/O Master’s base

## Slide 37: Do-more Architecture (3) Module Configuration – ERM100 Module
ERM100 Module
@ERM_001
Do-more Memory
DLRX
RD/WT
@ERM_001 Device interfaces directly to the ERM100 via the @LocalIOMaster handling the ERM100 module communications
@ERM_001 Device provides interface to the ERM100 for the DLRX, RD/WT instructions
DLRX, RD/WT instructions use Do-more memory for parameters
@ERM_001 Device provides a uniform interface to the ERM100 for Do-more Memory
Must use ERM Workbench to Configure:
EBC100 Slaves & their I/O Configurations
The @ERM_001 Device is automatically created when an ERM100 module is plugged into an I/O Master’s base

## Slide 38: Do-more Architecture (3) Module Configuration – F2-8AD4DA-x Analog Combo Module
F2-8AD4DA-x Module
I/O Master Device
I/O Memory
Instructions
The I/O Master Device interfaces directly to the F2-8AD4DA-x module handling the module communications & allowing the settings to be written on power-up
The instructions have access to the mapped I/O memory of the F2-8AD4DA-x module
The I/O Master Device provides a uniform interface to the F2-8AD4DA-x module by mapping its I/O to I/O memory
Module Settings:
Enable channel
Resolution
Track & hold
Input/Output range
A Module Configuration is automatically created when an F2-8AD4DA-x module is plugged into an I/O Master’s base

## Slide 39: Do-more Architecture (3) Module Configuration – GS-EDRV100 Module
GS-EDRV100 Module
@GS2_100
$GS2_100
Do-more Memory
GSREGRD
GSREGWR
@GS2_100 Device interfaces directly to the GS-EDRV100 module via the Ethernet I/O Master handling the GS-EDRV100 module communications
@GS2_100 Device provides interface to the hardware for the GSREGRD & GSREGWR instructions
Instructions use Do-more memory for parameters
@GS2_100 Device provides a uniform interface to the GS-EDRV100 for the $GS2_100 Structure
The @GS2_100 Device is automatically created when a GS-EDRV100 module is configured as a slave to an Ethernet I/O Master

## Slide 40: (3) Module Configuration
SERIO/SERIO4 (@SERIO_004_A, _B, _C)
  Do-more Programming
    Allows access to all Do-more memory
    Uses $SERIO_004_A, _B, _C memory structure
  K-sequence Server
    Allows access to DL-memory
    Uses $SERIO_004_A, _B, _C memory structure
  Modbus RTU Server (Slave)
    Allows access to M-memory
    Uses $SERIO_004_A, _B, _C memory structure
  Modbus RTU Client (Master)
    Used by MRX/MWX instructions
  General Purpose
    Used by STREAMIN/STREAMOUT instructions
    Uses $SERIO_004_A, _B, _C memory structure
Terminator Analog Output
  Allows configuration of enable, output type/range

## Slide 41: Do-more Architecture (3) Module Configuration – Do-more Programming
SERIO/SERIO4 Module
All PLC Memory
$SERIO_001_A
Do-more Server on @SERIO_001_A
Do-more Server runs in the background
Do-more Server interfaces directly to the SERIO/SERIO4 Module via the @LocalIOMaster Device
Do-more Server provides a uniform interface to the SERIO/SERIO4 Module for all the PLC’s memory & $SERIO_001_A Structure
Serial Port Settings:
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control
The @SERIO_001_A Device is automatically created when a SERIO/SERIO4 module’s Port A is configured as “Do-more Programming”

## Slide 42: Do-more Architecture (3) Module Configuration – DL Server (K-seq)
SERIO/SERIO4 Module
DL-Memory
$SERIO_001_A
DL Server on @SERIO_001_A
DL Server runs in the background
DL Server interfaces directly to the SERIO/SERIO4 Module via the @LocalIOMaster
DL Server provides a uniform interface to the SERIO/SERIO4 Module for DL memory & $SERIO_001_A
Serial Port Settings:
Station
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control
The @SERIO_001_A Device is automatically created when a SERIO/SERIO4 module’s Port A is configured as “K-Sequencer Server”

## Slide 43: Do-more Architecture (3) Module Configuration – Modbus RTU Server (Slave)
SERIO/SERIO4 Module
M-Memory
$SERIO_001_A
Modbus RTU Server on @SERIO_001_A
Modbus RTU Server runs in the background but is visible & configurable
Modbus RTU Server interfaces directly to the SERIO/SERIO4 Module via the @LocalIOMaster
Modbus RTU Server provides a uniform interface to the SERIO/SERIO4 Module for M-memory & $SERIO_001_A
Modbus RTU Server Settings:
Unit ID
Baud Rate
Data Bits
Stop Bits
Parity
Transmit Control
RTS Control
The @SERIO_001_A Device is automatically created when a SERIO/SERIO4 module’s Port A is configured as “Modbus RTU Server (Slave)”

## Slide 44: Do-more Architecture (3) Module Configuration – Modbus RTU Client (Master)
SERIO/SERIO4 Module
@SERIO_001_A
Do-more Memory
MRX
MWX
@SERIO_001_A Device interfaces directly to the SERIO/SERIO4 Module handling the Modbus RTU protocol
@SERIO_001_A Device provides interface to the SERIO/SERIO4 Module for the MRX/MWX instructions
Modbus RTU Client Configuration:
Timeout
Retries
Inter-packet Delay
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
MRX/MWX instructions use Do-more memory for parameters
The @SERIO_001_A Device is automatically created when a SERIO/SERIO4 module’s Port A is configured as “Modbus RTU Client (Master)”

## Slide 45: Do-more Architecture (3) Module Configuration – General Purpose
SERIO/SERIO4 Module
@SERIO_001_A
$SERIO_001_A
Do-more Memory
STREAMIN
STREAMOUT
@SERIO_001_A Device interfaces directly to the SERIO/SERIO4 Module handling the general purpose comms
@SERIO_001_A Device provides interface to the SERIO/SERIO4 Module for the STREAMIN/STREAMOUT instructions
Serial Port Settings:
Baud rate
Data bits
Stop bits
Parity
Transmit control
RTS control
STREAMIN/STREAMOUT instructions use Do-more memory for parameters
@SERIO_001_A Device provides a uniform interface to the SERIO/SERIO4 Module for the $SERIO_001_A Structure
The @SERIO_001_A Device is automatically created when a SERIO/SERIO4 module’s Port A is configured as “General Purpose”

## Slide 46: Do-more Architecture (3) Module Configuration – T1F-16DA-x Analog Output Module
T1F-16DA-x Module
I/O Master Device
I/O Memory
Instructions
The I/O Master Device interfaces directly to the T1F-16DA-x module handling the module communications & allowing the settings to be written on power-up
The instructions have access to the mapped I/O of the T1F-16DA-x module
The I/O Master Device provides a uniform interface to the T1F-16DA-x module by mapping its I/O to I/O memory
Module Settings:
Enable channel
Output range type
Output range (voltage)
Output range (current)
A Module Configuration is automatically created when a T1F-16DA-x module is plugged into an I/O Master’s base

## Slide 47: (4) Device Configuration
System Devices
  Do-more Logger (@DMLogger)
    Used by STREAMOUT instruction
  EtherNet/IP Explicit Message Client (@IntEIPClient)
    Used by EIPMSG instruction
  Do-more Ethernet Peer-to-Peer Client (@IntEthDMPPClient)
    Used by RX/WX instructions
  Modbus TCP Client (@IntModTCPClient)
    Used by MRX/MWX instructions
  User Log (@UserLog)
    Used by STREAMOUT instruction
  DL Client (@IntEthernet)
    Used by DLRX/DLWX instructions

## Slide 48: Do-more Architecture (4) Device Configuration – Do-more Logger
Internal Ethernet Port
@DMLogger
Do-more Memory
STREAMOUT
@DMLogger Device interfaces directly to the Internal Ethernet Port handling the broadcasts to Do-more Logger App
@DMLogger Device provides interface to the Internal Ethernet Port for the STREAMOUT instruction
The STREAMOUT instruction uses Do-more memory for parameters

## Slide 49: Do-more Architecture (4) Device Configuration – EtherNet/IP Explicit Message Client (Master)
Internal Ethernet Port
@IntEIPClient
Do-more Memory
EIPMSG
@IntEIPClient Device interfaces directly to the Internal Ethernet Port handling the EtherNet/IP Explicit Message protocol
@IntEIPClient Device provides interface to the Internal Ethernet Port for the EIPMSG instruction
The EIPMSG instruction uses Do-more memory for parameters

## Slide 50: Do-more Architecture (4) Device Configuration – Do-more Peer-to-peer Client
Internal Ethernet Port
@IntEthDMPPClient
Do-more Memory
RX
WX
@IntEthDMPPClient Device interfaces directly to the Internal Ethernet Port handling the Do-more Point-to-Point protocol
@IntEthDMPPClient Device provides interface to the Internal Ethernet Port for the RX/WX instructions
The RX/WX instructions use Do-more memory for parameters
NOTE: The Do-more Point-to-Point Server portion is handled by the Do-more Server (see above)

## Slide 51: Do-more Architecture (4) Device Configuration – Modbus TCP Client (Master)
Internal Ethernet Port
@IntModTCPClient
Do-more Memory
MRX
MWX
@IntModTCPClient Device interfaces directly to the Internal Ethernet Port handling the Modbus TCP protocol
@IntModTCPClient Device provides interface to the Internal Ethernet Port for the MRX/MWX instructions
Modbus TCP Client Configuration:
Timeout
Retries
Inactivity Timeout
MRX/MWX instructions use Do-more memory for parameters

## Slide 52: Do-more Architecture (4) Device Configuration – User Log
Internal User Event Log
@UserLog
Do-more Memory
STREAMOUT
@UserLog Device interfaces directly to the Internal User Event Log handling the data being written there
@UserLog Device provides interface to the Internal User Event Log for the STREAMOUT instruction
The STREAMOUT instruction uses Do-more memory for parameters

## Slide 53: Do-more Architecture (4) Device Configuration – DL Client (K-seq)
Internal Ethernet Port
@IntEthernet
Do-more Memory
DLRX
DLWX
@IntEthernet Device interfaces directly to the Internal Ethernet Port handling the DL (K-seq) communications
@IntEthernet Device provides interface to the Internal Ethernet Port for the DLRX/DLWX instructions
DLRX/DLWX use Do-more memory for parameters

## Slide 54: (4) Device Configuration
User Devices
  EtherNet/IP Explicit Message Client (e.g. @MyEIPClient)
    Used by EIPMSG instruction
  Modbus TCP Client (e.g. @MyModTCPClient)
    Used by MRX/MWX instructions
  SMTP Client (e.g. @MySMTPClient)
    Used by EMAIL instruction
  TCP Client (e.g. @MyTCPClient)
    Uses $MyTCPClient memory structure
    Used by OPENTCP, STREAMIN/STREAMOUT instructions
  TCP Server (e.g. @MyTCPServer)
    Uses $MyTCPServer memory structure
    Used by TCPLISTEN, STREAMIN/STREAMOUT instructions
  UDP Connection (e.g. @MyUDPConnect)
    Uses $MyUDPConnect memory structure
    Used by PACKETIN/PACKETOUT instructions

## Slide 55: Do-more Architecture (4) Device Configuration – Extra EtherNet/IP Explicit Message Client
Internal Ethernet Port
@MyEIPClient
Do-more Memory
EIPMSG
@MyEIPClient Device interfaces directly to the Internal Ethernet Port handling the EtherNet/IP Explicit Message protocol
@MyEIPClient Device provides interface to the Internal Ethernet Port for the EIPMSG instruction
The EIPMSG instruction uses Do-more memory for parameters

## Slide 56: Do-more Architecture (4) Device Configuration – Extra Modbus TCP Client (Master)
Internal Ethernet Port
@MyModTCPClient
Do-more Memory
MRX
MWX
@MyModTCPClient Device interfaces directly to the Internal Ethernet Port handling the Modbus TCP protocol
@MyModTCPClient Device provides interface to the Internal Ethernet Port for the MRX/MWX instructions
Modbus TCP Client Configuration:
Timeout
Retries
Inactivity Timeout
MRX/MWX instructions use Do-more memory for parameters

## Slide 57: Do-more Architecture (4) Device Configuration – SMTP Client (Email)
Internal Ethernet Port
@MySMTPClient
Do-more Memory
EMAIL
@MySMTPClient Device interfaces directly to the Internal Ethernet Port handling the SMTP protocol
@MySMTPClient Device provides interface to the Internal Ethernet Port for the EMAIL instructions
SMTP Client Configuration:
SMTP Server IP Address
SMTP Server Port
Timeout
‘From’ Email Address
Authentication
EMAIL instructions use Do-more memory for parameters

## Slide 58: Do-more Architecture (4) Device Configuration – TCP Client
Internal Ethernet Port
@MyTCPClient
$MyTCPClient
Do-more Memory
OPENTCP
STREAMIN
STREAMOUT
@MyTCPClient Device interfaces directly to the Internal Ethernet Port handling TCP protocol
@MyTCPClient Device provides interface to the Internal Ethernet Port for the OPENTCP, STREAMIN & STREAMOUT instructions
OPENTCP, STREAMIN & STREAMOUT instructions use Do-more memory for parameters
@MyTCPClient Device provides a uniform interface to the Internal Ethernet Port for the $MyTCPClient Structure

## Slide 59: Do-more Architecture (4) Device Configuration – TCP Server
Internal Ethernet Port
@MyTCPServer
$MyTCPServer
Do-more Memory
TCPLISTEN
STREAMIN
STREAMOUT
@MyTCPServer Device interfaces directly to the Internal Ethernet Port handling the TCP protocol
@MyTCPServer Device provides interface to the Internal Ethernet Port for the TCPLISTEN, STREAMIN & STREAMOUT instructions
TCP Server Configuration:
TCP Port Number
TCPLISTEN, STREAMIN & STREAMOUT instructions use Do-more memory for parameters
@MyTCPServer Device provides a uniform interface to the Internal Ethernet Port for the $MyTCPServer Structure

## Slide 60: Do-more Architecture (4) Device Configuration – UDP Connection
Internal Ethernet Port
@MyUDP
$MyUDP
Do-more Memory
PACKETIN
PACKETOUT
@MyUDP Device interfaces directly to the Internal Ethernet Port handling the UDP protocol
@MyUDP Device provides interface to the Internal Ethernet Port for the PACKETIN & PACKETOUT instructions
UDP Server Configuration:
UDP Port Number
PACKETIN & PACKETOUT instructions use Do-more memory for parameters
@MyUDP Device provides a uniform interface to the Internal Ethernet Port for the $MyUDP Structure

## Slide 61: (5) I/O Mappings
Auto mode automatically assigns X/Y/WX/WY addressing in sequential order
  Addresses are shown in gray
Manual mode allows editing of the start address for each module
  Addresses are shown in black
  Address overlaps show in red
  Addresses exceeding memory range are bold red
  A base’s default map can be changed

## Slide 62: (6) Memory Configuration
Memory Blocks
  Indexable
    E.g. Fred0, Fred1, Fred2, etc.
  Common data type
    E.g. bits, numeric, structure
  Referenced by name & index
    E.g. Fred0, Fred[V15]
  Cannot be created while editing ladders
Heap Items (single instance)
  Not indexable
    E.g. Fred, Wilma, Barney, etc.
  Common data type
    Structure only
  Referenced by name (no index)
    E.g. Fred, Wilma, Barney, etc.
  Can be created while editing ladders
    NOTE: Cannot download in RUN mode (System Configuration changed)

## Slide 63: Point #1: Device-centric
Hardware or System Resource
Device
Memory
Instruction
Server

## Slide 64: Point #2: Configuration Hierarchy
CPU Configuration
I/O Configuration
Module Configuration(s)
Device Configuration
I/O Mappings
Memory Configuration