## Slide 1: Do-more Technical Training
Instruction Set
(Program Control)

## Slide 2: Instruction Set (Program Control)
Program Control
  ENTASK
  EXIT
  GOTO
  HALT
  JMP (Stage)
  JMPI (Stage)
  LABEL
  REBOOT
  RESTART
  RUN
  SG (Stage)
  SGCONVRG (Stage)
  SGDIVRG (Stage)
  SGRST (Stage)
  SGRSTR (Stage)
  SGSET (Stage)
  STOP
  SUSPEND
  WATCHDOG
  YIELD

## Slide 3: Instruction Set (Program Control)
GOTO “Go To Label”
  Immediate branch to LABEL instruction
    Cannot reference Labels in a different Program/Task
    If inside FOR/NEXT, WHILE/WEND, or REPEAT/UNTIL loop, cannot target Labels outside that loop
    Cannot target Labels in a different stage
    Branching backward subjects it to yielding (blue)
LABEL “Program Label”
  The target of the GOTO instruction

## Slide 4: Instruction Set (Program Control)
REBOOT “Reboot PLC”
  Causes CPU to perform a cold reboot (just like a power cycle)

## Slide 5: Instruction Set (Program Control)
RESTART “Restart Program or Task”
  Stops Program or Task then restarts it so that it begins running from the beginning
    Resets Stages, clears internal flags, counters, etc.

## Slide 6: Instruction Set (Program Control)
STOP “Switch to Program Mode”
  Causes CPU to go to STOP (Program) Mode
    Since there is no way, of course, to programmatically switch back to RUN Mode, this could be a safety concern

## Slide 7: Instruction Set (Program Control)
SUSPEND “Suspend Program or Task”
  Suspends the target Program or Task from running
    The current state of all ladder logic in target is maintained
    .InstrSuspend = ON
    Name of target is shown in yellow
    Cannot suspend itself

## Slide 8: Instruction Set (Program Control)
WATCHDOG “Force Watchdog Error”
  Generates a software or hardware watchdog error
    Used to verify emergency shutdown
    Parameters:
      Fire Software Watchdog
        CPU goes to STOP (Program) Mode
        Acts like scantime > $WatchdogTimeVal (DST23)
      Fire Hardware Watchdog
        Depends on setup of $DisableHwWdog (ST25) & $HwWatchdogMode (ST24)
    If input logic is retentive & Mode switch is in RUN or TERM, CPU will execute Force Watchdog Error instruction continuously.
      Place Mode switch in STOP to break out of this

## Slide 9: Instruction Set (Program Control)
YIELD “Yield Program or Task”
  Stops execution of current Program or Task & passes control to next code block in the execution order
    Yields (blue triangle) regardless of value in .TimeSlice
    Code block continues at instruction directly below upon next execution
    Used so scantime can be controlled
      E.g. Program normally takes long time to complete
        Inserting YIELDs in the code breaks it up
1st scan
2nd scan
Notes: Clear PLC
Create MyProgram
  Add $On  4 MATHs, R100 = SQRT(1.0 / (1.0 / (1.0 / (SIN(RAD(R0))**2))))
To $Main, add X0  RUN MyProgram
To $tTopOfScan add MATH D2 = TICKus()
To $tBottomOfScan add MATH D3 = TICKus() – D2
Create Data View: X0, D3, R0
  Write a value to R0 (for the MATH in MyProgram, so it won’t generate a divide-by-zero)
Download & put into RUN
X0 = ON
  Notice the value of D3 in µs
Edit MyProgram and put a YIELD in between the 4 MATHs (2 above, 2 below)
Download, notice the smaller D3
Edit MyProgram and put 2 more YIELDs for all 4 MATHs
Download, notice the smaller D3

## Slide 10: Stage Programming
Introduction to sequencing
  Ladder logic
    Pros:
      Very good at controlling concurrent processes
    Cons:
      Not good at controlling sequential processes
      Not good at event-driven sequences
      Programs get filled with numerous interlocking bits
      Difficult to debug
      Difficult to modify
      All logic impacts scantime

## Slide 11: Stage Programming
Ladder Program
  States of Y0
    OFF
    ON
  Initially Y0 = OFF
  X0 causes Y0 to transition to ON state
  X1 causes Y0 to transition to OFF state

## Slide 12: Stage Programming
State Diagram
  States of Y0
    OFF
    ON
  Initially Y0 = OFF
  X0 causes Y0 to transition to ON state
  X1 causes Y0 to transition to OFF state
OFF
ON
Y0
X0
X1
OFF
ON

## Slide 13: Stage Programming
Sequence Diagram
  States of Y0
    OFF
    ON
  Initially Y0 = OFF
  X0 causes Y0 to transition to ON state
  X1 causes Y0 to transition to OFF state

## Slide 14: Stage Programming
Stage Program
  States of Y0
    OFF
    ON
  Initially Y0 = OFF
  X0 causes Y0 to transition to ON state
  X1 causes Y0 to transition to OFF state

## Slide 15: Stage Programming
Numbering
  Tasks do not have Stages
  Programs can have 128 Stages (SG; S0-S127) each
  Stage number does not determine sequence
The Initial Stage is the first one (very top)
Enabling/Disabling
  Enabled Stages are executed each PLC scan
  When a Stage is enabled/scanned the first time it artificially generates an “edge” for all the edge-triggered instructions by setting Edge bits for each bit in the Stage that is already ON when the Stage was enabled*
  Disabled Stages are not scanned
  A disabled Stage runs a “Termination Scan” immediately following the scan in which it was disabled
  *Exception: Bits associated with Counter instructions

## Slide 16: Stage Programming
Edge Bits
  Normally hidden system-only bits
  Internal use only; cannot be modified by user
  Automatically added to project by Do-more Designer as edge-triggered instructions are programmed and assigned an index of zero (/E0)
  Actual usable index value (e.g. “21” of “/E21”) is assigned by the Do-more PLC when project is downloaded (i.e. the PLC, not Do-more Designer, assigns them)
  Holds the scan-to-scan state of edge-triggered inputs
  When an edge is detected (e.g. OFF-to-ON or ON-to-OFF, depending on instruction) the associated Edge Bit is set ON for internal use
Automatic Edge Bit Feature in Stages
  Edge Bits have a special use in Stages due to a desired feature
  When a particular Stage is enabled, if there is an edge-triggered instruction that gets scanned in that stage, the Edge Bit for that instruction is automatically set ON if that input was ON when the Stage was enabled
    Thus what would normally take a minimum of 2-3 scans of that particular Stage to detect an edge for that instruction is actually “detected” (by this feature) on the 1st scan in which that Stage is enabled
S10 Disabled
Rung not scanned
C0 = OFF
S10 Enabled
1
/E0
/E21
2
It took a minimum of 2 scans in order for S10 to “see” C0’s edge. This is normal.
But what if C0 had been ON when S10 was enabled instead of OFF as in this example?
S10 Disabled
S10 Enabled
OFF-to-ON not yet seen because C0 was ON when S10 was enabled
C0 = OFF
OFF-to-ON not yet seen because C0 has just now gone OFF
C0 = ON
3
It took a minimum of 3 scans in order for S10 to “see” C0’s edge.
But this is NOT the way Do-more works!
It only takes 1 scan in order for S10 to “see” C0’s edge if C0 was ON when S10 was enabled. This is because C0’s Edge Bit is automatically set ON as a feature in Do-more
NOTE: This Automatic Edge-Bit Feature is not applied to Counter instructions CNT, CNTDN, UDC or UDCG. These are the ONLY exceptions.

## Slide 17: Stage Programming
Edge Bits
  Since indexes are assigned at download time, Do-more Designer doesn’t “know” what those are until the project is read back up
  All Edge Bits in Do-more Designer originally have an index of zero (e.g. /E0)
  Thus the following two interesting scenarios can occur:
    (1) If a new project with edge-triggered instructions is first saved to disk and then downloaded to the PLC, a dialog will appear describing, “The Program has been modified…” when no manual modification occurred.
      Solution: Save the Project to Disk.
      If Project is not saved to disk then “Modified project not saved to disk – new Edge/Instruction IDs assigned during download to PLC” is displayed in the Output Window as a Warning
    (2) If that project (which was not saved) is closed and then reopened online, the compare will fail.
      If <Compare Programs…> is used the Edge Bit difference is shown
      Solution: Go online with the PLC project and save the project to disk with the new Edge Bit index assignments
/E0
/E21

## Slide 18: Stage Programming
Termination Scan
  Scan which immediately follows the scan in which the Stage was last executed
  Insures proper shutdown
  Insures subsequent startup behavior
  What happens?
    OUT instructions are turned OFF
    Timers & Counters are reset*
    Edge bits are turned OFF
    *UDCG “Global Up/Down Counter” not reset
    *TMRAG “Global Accumulating Timer” not reset

## Slide 19: Stage Programming
Enabling:
  When the Stage is the target of:
    (1) JMP “Jump To Stage”
    (2) JMPI “Indexed Jump”
    (3) SGSET “Enable Stage”
    (4) SGDIVRG “Jump to Multiple Stages”
    (5) SGCONVRG “Converge Multiple Stages to SG”
Disabling:
  When the Stage is:
    The source of:
      (1) JMP “Jump To Stage”
      (2) JMPI “Indexed Jump”
      (4) SGDIVRG “Jump to Multiple Stages”
      (5) SGCONVRG “Converge Multiple Stages to SG”
    The target of:
      (6) SGRST “Disable Stage”
      (7) SGRSTR “Disable Range of Stages”

## Slide 20: Stage Programming
JMP “Jump To Stage”
  Disables Stage in which it is contained & enables the “jump-to” Stage
  Parameters:
    Transition To – target Stage to “jump” to
  NOTES:
    Does not “jump” immediately
    Code between the JMP and end of the Stage is still scanned / executed
    Cannot “jump” to Stages in other Programs

## Slide 21: Stage Programming
JMPI “Indexed Jump”
  Disables Stage in which it is contained & enables the “jump-to” Stage based on an Index
  Parameters:
    Index – memory location of index value
    First Stage – 1st Stage in range for index = 0
    Last/Exception Stage – Stage to “jump” to if index is out of range
  NOTES:
    Does not “jump” immediately
    Code between the JMPI and end of the Stage is still scanned / executed
    Cannot “jump” to Stages in other Programs

## Slide 22: Stage Programming
SGSET “Enable Stage”
  Enables target Stage
  Parameters:
    Stage – target Stage to enable
  NOTES:
    Does not disable Stage containing SGSET
    Cannot enable Stages in other Programs

## Slide 23: Stage Programming
SGRST “Disable Stage”
  Disables target Stage
  Parameters:
    Stage – target Stage to disable
  NOTES:
    If it disables itself, code between the SGRST & end of the Stage is still scanned / executed
    Cannot disable Stages in other Programs

## Slide 24: Stage Programming
SGRSTR “Disable Range of Stages”
  Disables a range of Stages
  Parameters:
    Start Stage – 1st Stage in range to disable
    End Stage – last Stage in range to disable
  NOTES:
    If it disables itself, code between the SGRSTR & end of the Stage is still scanned / executed
    Cannot disable Stages in other Programs

## Slide 25: Stage Programming
SGDIVRG “Jump to Multiple Stages”
  Disables Stage in which it is contained & enables all Stages listed
  Parameters:
    Transition To – list of Stages to enable
  NOTES:
    Cannot disable Stages in other Programs

## Slide 26: Stage Programming
SGCONVRG “Converge Multiple Stages to SG”
  Disables listed Stages & enables target Stage based on condition
  Parameters:
    Stage – target Stage to be enabled
    From Stages – list of Stages to be disabled when condition is true
    Then converge when – condition causing the convergence
  NOTES:
    Cannot use Stages in other Programs

## Slide 27: Stage Programming
Design Stage Program
Drill Head
UP
DN
X1 is the Drill Head’s start position
X2 is the Drill Head’s drill position
X3 is the drill bit’s position
Y0 drives the Drill Head out
Y1 spins the drill
Y2 extends the drill bit
X0 starts the Drill Operation
Y3 determines direction of Drill Head

## Slide 28: Stage Programming
Design Stage Program
  Inputs:
    X0: Start drilling operation
    X1: Drill Head in start position
    X2: Drill Head in drilling position
    X3: Drill bit is down
  Outputs:
    Y0: Traverse motor
    Y1: Drill bit motor
    Y2: Extend drill bit
    Y3: Traverse direction

## Slide 29: Stage Programming
Design Stage Program
  How do we naturally think about it?
  We think of it as a sequence (stage)
    Wait for operator to press START button to begin drilling operation
    When START button is pressed, drill head traverses to drilling position
    When drilling position is reached, drill spins up
    After drill spins up, drilling operation is performed
    After drilling operation is performed, drill is retracted & turned off
    After drill is retracted, drill head is retrieved back to starting position
  Is ladders the best option? Probably not.
  Could possibly be done with DRUM instruction because it is discrete I/O and timers that are used
    But if anything else is done during each stage of the sequence, a DRUM instruction could not be utilized

## Slide 30: Stage Programming
Design Stage Program (Ladders)
Interlocking C-bits are necessary to sequence the Ladder Logic

## Slide 31: Stage Programming
Design Stage Program (Stage)
Interlocking C-bits are not necessary
Initial Stage
Waits for: - Drill head in start position
Drill head not in drilling position
Drill bit is not down
- Operator to press START
Jumps to “Goto Drill Position”
Sets Direction for “out” and turns traverse motor ON
When drilling position is reached, jumps to spin up the drill
When the jump occurs both the DirectionOut and Traverse Motor automatically turn OFF

## Slide 32: Stage Programming
Design Stage Program (Stage)
Drill motor is turned ON & allowed to spin up for 1 second
When drill has spun up for 1 second, jumps to “Drill”
Drill bit is extended to do the drilling operation
When drill bit has reached down position, jumps to “retract the drill bit”
When jump occurs the drill motor is left spinning because a SET was used (instead of an OUT)
When jump occurs the extend drill bit mechanism automatically turns OFF

## Slide 33: Stage Programming
Design Stage Program (Stage)
Drill bit is allowed time to retract for 1 second
When drill bit is no longer down & 1 second has passed, drill motor is turned OFF
Time to retrieve the Drill Head & start over
Traverse motor is turned ON to retrieve Drill Head back to start position
When Drill Head reaches start position, jump is made back to START
When jump occurs the traverse motor is automatically shut OFF