## Slide 1: Do-more Technical Training
Instruction Set
(String)

## Slide 2: Instruction Set (String)
STR2INT “Convert String to Integer”
  Converts ASCII digits to integer value
  Parameters:
    Input String – string to be converted
    Input Radix – determines valid characters
      Decimal (base 10): characters “0-9”
      Hexadecimal (base 16): characters “0-F”
      Octal (base 8): characters “0-7”
      Implied Base: characters “0x” (hex), “0” (octal), “1-9”(decimal)
      Other (2-36): e.g. 36 would validate characters “0-Z”
    Numeric Output – location of converted value
    Index Where Stopped – character location in string
  NOTES:
    If Input String is empty then Index Where Stopped = -1; ERR = “STR2INT input string is empty”
    If Input String contains invalid characters then Index Where Stopped = -1; ERR = “STR2INT input string couldn’t be converted to an integer value”
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Input Radix | Numeric Output | Index Where Stopped
Decimal | 0 | -1
Hexadecimal | 0 | -1
Octal | 0 | -1
Implied Base | 0 | -1
Other: 20 | 0 | -1
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | 1 | 0 |  |  |  |  |  |  | 
Input Radix | Numeric Output | Index Where Stopped
Decimal | 10 | 2
Hexadecimal | 16 | 2
Octal | 8 | 2
Implied Base | “Decimal”  10 | 2
Other: 20 | 20 | 2
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 |  |  |  | 1 | 0 |  |  |  | 
Input Radix | Numeric Output | Index Where Stopped
Decimal | 10 | 5
Hexadecimal | 16 | 5
Octal | 8 | 5
Implied Base | “Decimal”  10 | 5
Other: 20 | 20 | 5
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 |  |  |  | 1 | F |  |  |  | 
Input Radix | Numeric Output | Index Where Stopped
Decimal | 1 | 4
Hexadecimal | 31 | 5
Octal | 1 | 4
Implied Base | “Decimal”  1 | 4
Other: 20 | 35 | 5
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 | @ |  |  |  |  |  |  |  | 
Input Radix | Numeric Output | Index Where Stopped
Decimal | 0 | -1
Hexadecimal | 0 | -1
Octal | 0 | -1
Implied Base | 0 | -1
Other: 20 | 0 | -1

## Slide 3: Instruction Set (String)
STR2REAL “Convert String to Real”
  Converts ASCII digits to real value
  Parameters:
    Input String – string to be converted
    Numeric Output – location of converted value
    Index Where Stopped – character location in string
  NOTES:
    Valid characters are: “0123456789.E+-”
    If Input String is empty then Index Where Stopped = -1; ERR = “STR2REAL input string is empty”
    If Input String contains invalid characters then Index Where Stopped = -1; ERR = “STR2REAL input string couldn’t be converted to an integer value”
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 |  |  |  | 1 |  |  |  |  |  | 
Numeric Output | Index Where Stopped
1.0 | 4
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 |  |  |  | - | 3 | . | 1 | 4 |  | 
Numeric Output | Index Where Stopped
-3.14 | 8
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 | + | 6 | . | 0 | 2 | E | + | 2 | 3 | 
Numeric Output | Index Where Stopped
6.02E+23 | 9
SS0 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
 |  |  |  | . |  |  |  |  |  | 
Numeric Output | Index Where Stopped
0.0 | -1

## Slide 4: Instruction Set (String)
STRCASE “Convert String to UPPER/lower Case”
  Converts all characters in a string to either upper case or lower case letters
  Parameters:
    Input/Output String – string to be converted
    Convert to:
      all lower case
      ALL UPPER CASE
  NOTES:
    Valid characters are only alphabetic letters
    If character is not alphabetic, no change occurs to that character
SS0 | a | b | c | d | ! | E | F | g | H
SS0 | a | b | c | d | ! | e | f | g | h
Low
SS0 | A | B | C | D | ! | E | F | G | H
Up

## Slide 5: Instruction Set (String)
STRCLEAR “Clear Strings”
  Deletes all characters from a single string or a range of strings
  Parameters:
    Start String – 1st (or only) string to be cleared
    Number of Strings to Clear – 1 to 65535 (or variable)
  NOTES:
    The Status display will only show as many characters that fit in its borders (about 50 characters)

## Slide 6: Instruction Set (String)
STRCMP “String Compare”
  Compares two strings to determine if they are equal, less than or greater than
  Less than & greater than values are determined by the ASCII byte values
  Each byte position is compared until:
    Byte values don’t match with one value > or <
    End of one string reached 1st meaning it is <
    End of both strings reached simultaneously meaning equality
  Parameters:
    First String
    Case Sensitive:
      Yes, upper/lower case are different
      No, upper/lower case are equal
    Set If Equal (optional)
    Set If Less Than (optional)
    Set If Greater Than (optional)
    Second String or Text – the 2nd string can be a literal text in quotes
    Input Leg:
      Edge triggered
      Power flow enabled
SS0 | a | b | c | d | ! | E | F | g | H
SS1 | a | b | c | d | ! | E | F | g | H
Yes, upper/lower case are different |  | 
SS0 = SS1 | SS0 < SS1 | SS0 > SS1
YES |  | 
No, upper/lower case are equal |  | 
YES |  | 
SS0 | a | b | c | d | ! | E | F | g | H
SS1 | a | b | c | d | ! | E |  |  | 
Yes, upper/lower case are different |  | 
SS0 = SS1 | SS0 < SS1 | SS0 > SS1
 |  | YES
No, upper/lower case are equal |  | 
 |  | YES
SS0 | a | b | c | d | ! | E | F | g | H
SS1 | a | b | c | d | ! | e | F |  | 
Yes, upper/lower case are different |  | 
SS0 = SS1 | SS0 < SS1 | SS0 > SS1
 | YES | 
No, upper/lower case are equal |  | 
 |  | YES
E = 45 hex
e = 65 hex
SS0’s E is < SS1’s e
SS0’s E & SS1’s e are equal in value & SS0 is longer

## Slide 7: Instruction Set (String)
STRDELETE “Delete Substring”
  Deletes characters from a string
  Trailing characters are shifted to take the place of deleted ones
  Parameters:
    Input / Output String
    Starting at Offset: 0 – 1023 (or variable)
      The 1st character is 0 (zero)
    Number of Characters to Delete
SS0 | a | b | c | d | ! | E | F | g | H
To delete the ! character:
Starting at Offset = 4
Number of Characters to Delete = 1
0
1
2
3
4
SS0 | a | b | c | d | E | F | g | H | 

## Slide 8: Instruction Set (String)
STRFIND “Find within String”
  Search a target string for a particular string
  If successful the where-found offset could be used in STRSUB, STRDELETE or STRINSERT instructions
  Parameters:
    Find within – string in which to search
    Search from:
      Beginning to end
      End to beginning
    Case Sensitive:
      Yes, upper/lower case are different
      No, upper/lower case are equal
    In Offset: Start / Out Offset: Where Found – will contain -1 if nothing is found
    Set if found (optional)
    Set if NOT found (optional)
    Find Text/String:
      Exact sequence
      Any one of these characters – text box
    Input Leg:
      Edge triggered / Power flow enabled
SS0 | a | b | c | e | E | E | F | g | H
To find the E character:
Search from: Beginning to end
Case Sensitive: Yes
Find Text/String: Any one of these characters: “E”
0
1
2
3
4

## Slide 9: Instruction Set (String)
STRPUTB “Put Bytes Into a String”
  Puts bytes of data from a specified location range into a string
  Parameters:
    Put Into String – string that will contain data bytes
    Start at Index – 1st location in the string for the bytes
    Length in Bytes – number of bytes to write into string
    From Starting Element – 1st location to read bytes
    <Create Byte Buffer> button – convenient way to create a Memory Block of bytes (shows up in Memory Configuration)
  NOTES:
    Not intended to operate on strings with ASCII text

## Slide 10: Instruction Set (String)
STRGETB “Get Bytes Out of a String”
  Extracts bytes of data out of a string & stores them in specified location
  Parameters:
    Get out of String – string with data bytes
    Start at Index – 1st location in the string for the bytes
    Length in Bytes – number of bytes to copy
    Into Starting Element – 1st location to put extracted bytes
    <Create Byte Buffer> button – convenient way to create a Memory Block of bytes (shows up in Memory Configuration)
  NOTES:
    Not intended to operate on strings with ASCII text
Values are manually written to a custom byte memory MyBuffer10-13.
The STRPUTB writes the range MyBuffer10-13 into SS0
The STRGETB writes the bytes in SS0 to the range MyBuffer0-3
ASCII values of 10, 20, 30 are not displayable characters.
40 decimal ASCII is (.

## Slide 11: Instruction Set (String)
STRINSERT “Insert Substring”
  Inserts characters into a string
  Parameters:
    Insert String or Text
    Into String
    Starting at Offset
      If > length of string, it is appended to string
      If > allowable size of the Into String, then:
        Text is appended to string
        $OutOfRange (ST132) = ON
        ERR = “Argument out of range in STRINSERT…”
The text “not ” is to be inserted into SS0 starting at offset 12.

## Slide 12: Instruction Set (String)
STRPRINT “Print to String”
  Writes text & formatted data into a string
  Parameters:
    Print to
    Append to String (optional)
    Automatically insert space after each term (optional)
    Print Script – text with optional embedded fields (text, control characters, strings, elements, formatting & string selection functions, raw data) – See next slide 
    Input Leg – Edge triggered / Power flow enabled

## Slide 13: Instruction Set (Ethernet)
STRPRINT “Print to String”
  Parameters:
    Print Script
      String Literals – ASCII text in double quotes (e.g. “Hi!”)
      Data Elements – (e.g. “The current count is” CT0.Acc)
      Control Characters
        $$  $
        $”  “
        $L  <LF> (line feed)
        $N  <CR><LF> (carriage return, line feed)
        $P  <FF> (form feed)
        $R  <CR> (carriage return)
        $T  <TAB> (tab)
        $hh  hh (any one-byte hex value)
      Formatting Functions [see Do-more Designer Help Topic DMD0168]
        FmtString – Sets length and/or justifies text within a string
        FmtBit – Formats bits’ values as a text instead of just 0 or 1
        FmtInt – Formats how an integer is represented in a string
        FmtReal – Formats how real numbers are represented in a string
        FmtTMR – Formats how Timer Accumulator values are represented in a string
        FmtDate – Formats how a Date stamp is represented in a string
        FmtTime – Formats how a Time stamp is represented in a string
        Lookup – Selects a string in a list to represent a value
        Raw – Places bytes of data from a data block into a string

## Slide 14: Instruction Set (String)
STRSUB “Get Sub-String”
  Copies characters from one string to another
  Parameters:
    Input String
    Starting Offset
    Offset From – Beginning / End
    Length – variable or Remainder of input string
    Output String
    Input Leg – Edge triggered / Power flow enabled

## Slide 15: Instruction Set (String)
STRTRIM “Trim Whitespace”
  Removes all whitespace characters from the beginning and/or end of a string
    What is “Whitespace”? 
      Space (ASCII 20 hex)
      Horizontal tab <TAB> (ASCII 09 hex)
      Carriage return <CR> (ASCII 0D hex)
      Line feed <LF> (ASCII 0A hex)
      Form feed <FF> (ASCII 0C hex)
      Vertical tab <VT> (ASCII 0B hex)
  Parameters:
    String
    Trim
      Leading (optional)
      Trailing (optional)

## Slide 16: Instruction Set (String)
STRTRUNC “Set String Length”
  Sets the length of a string
  Parameters:
    String
    Length
      If 0 (zero) or negative (-) clears string <empty string>
      If > string’s length then string is padded with nulls (0; not spaces) to reach the specified length
      If > string’s allowed length (e.g. >64 for SS, >256 for SL) then entire string is padded with nulls (0; not spaces) and…
        $BufferOverflow (ST140) = ON
        ERR: “Length was greater than max string length in STRTRUNC…”