## Slide 1: Do-more Technical Training
Memory Types

## Slide 2: Memory Types
(1) Physical I/O
(2) System Memory
(3) User Memory

## Slide 3: Memory Types
(1) Physical I/O
  Input
    Bit (X0-2047)*
    Word (WX0-255)*
  Output
    Bit (Y0-2047)*
    Word (WY0-255)*
  Specialty
    CTRIO/CTRIO2
      Module ($CTRIO_001) [30]
      Counter ($CTRIO_001_C1F1) [8]
      Pulse Catch ($CTRIO_001_C1F2) [3]
      Edge Timer ($CTRIO_001_C1F2) [8]
      Raw Out ($CTRIO_001_Out0) [2]
      Pulse Out ($CTRIO_001_Out0) [10]
      Discrete Out ($CTRIO_001_Out0) [3]
    SERIO/SERIO4 ($SERIO_001_A, _B, _C) [6]
    GSDrive ($GS1_100) [26]
*NOTE: Adjustable size
# of structure members

## Slide 4: Memory Types
(2) System Memory
  Bits (ST0-1023)
  Dword (DST0-511)
  Structures
    Date/Time (SDT0-7) [9]
    I/O Masters
      LocalIOMaster [4]
      $EthIOMaster [68]
    Peerlink (PL) [86]
    Programs (<Name>) [147]
    Tasks (<Name>) [15]
    Servers [4]
      $IntEIPServer
      IntSerialServer
      IntUSBServer
      ModbusTCPServer
    Stream [6]
      IntSerial
      <$Name>
    Packet (<$Name>) [3]
    PID (<$Name>) [19]
    Ramp/Soak (<$Name>) [5]
    Drum (<$Name>) [8]
    String [2]
      ERR
      LastERR0-7
      MSG
      LastMSG0-7
      PartNum
      SerialNum
      SysDesc
      SysName
# of structure members

## Slide 5: Memory Types
(3) User Memory1
  Bits
    C0-2047
    DLX0-7772
    DLY0-7772
    DLC0-7772
    MI0-1023
    MC0-1023
  Word
    Unsigned
      V0-4095
      PL0-255
      DLV0-37772
  1NOTE: Adjustable size
  2NOTE: Octal address
    Signed
      N0-4095
      MIR0-2047
      MHR0-2047
  Dword
    Signed (D0-4095)
    Real (R0-4095)
  Structures
    Timer (T0-255) [5]
    Counter (CT0-255) [5]
    Date/Time (UDT0-31) [9]
    String [2]
      Short (SS0-127)
      Long (SL0-63)
# of structure members

## Slide 6: Memory Types
Project Browser 
  Configuration 
    Memory

## Slide 7: Memory Types
Strong Typing
  Every element in the PLC has a data type
    (bit, real, unsigned word, timer structure, etc.)
  Strong Typing PRO: Instructions know the data types
    EXAMPLE:
      A signed double-word (D-memory) can be compared to a real number (R-memory) without conversion to the same data type
  Even constants are strongly typed
    EXAMPLES:
      Hexadecimal (prefix of “0x”; zero x)
      Decimal (the number itself)
      Octal (prefix of “0”; zero)
      Real (enter a decimal point with the number; e.g. 2.0)

## Slide 8: Memory Types
Casting
  Strong Typing CON: Sometimes Strong Typing “gets in the way”
    How to use just one bit in a V-memory location?
    How to look at a group of 16 discrete inputs as a word?
    How to look at 2 Modbus Holding Registers as a 32-bit Real number?
  Casting operator suffix “:” (colon) is the answer:
    V5:0 – look at bit 0 in V5
    X0:UB – look at X0-7 as an unsigned byte
    X16:UW – look at X16-31 as an unsigned word
    X32:SD – look at X32-63 as signed double-word
  Type boundaries must be observed (byte, word, double word):
    X1:UB – invalid, but X0:UB or X8:UB are valid
  More examples:
    MHR10:R – look at 32-bit MHR10-11 as 32-bit real
    V12:SD – look at 32-bit V12-13 as a signed double-word
    V11:B0 – look at byte 0 (low byte) of V11
    V11:UB1 – look at byte 1 (high byte) of V11 as an unsigned byte
  Use Element Browser <F9> (Search  Element Browser) & Cast Builder Tool to help build