## Slide 1: Do-more Technical Training
Project Management

## Slide 2: Project Management
Project File
Project Saving
Project Storage
Project Creation
Project Editing
DMD

## Slide 3: Project Management
Project File
  Filename: <MyProject>.DMD
  Contains everything:
    System Configuration
      CPU Configuration
      I/O Configuration
      Module Configuration
      Device Configuration
      I/O Mappings
      Memory Configuration
    Ladder logic program
      $Main Program
      System Tasks (used)
      Tasks (User)
      Programs (User)
    Documentation
      Project Filename
      Project Info
      Element Documentation
      Rung Comments
      Title Page
      *User Document
    *Memory Image
      Memory Image Config
      Memory Image Data
    *Print Options
* Not stored in the PLC
DMD

## Slide 4: Project Management
Project Saving
  File 
    Save Project
      Saves everything in current filename
    Save Project As…
      Saves everything in different filename
    Write Project to PLC
      Writes what has changed of System Config, Ladders, Documentation & optionally the Memory Image
Portions are highlighted that are about to be written to the PLC
If a Memory Image exists, it can be optionally downloaded
Only valid downloading options are available to choose from

## Slide 5: Project Management
Project Saving
  File 
    Export 
      Project… - Creates text-only version of ladder program (mnemonics), rung comments & element documentation. Designed for backup.
        Export
          Program Range (Entire, Specified)
            Include Code-Block Start/End instructions
          Configuration (System, Memory)
          Rung Comments (Unformatted, Formatted)
          Include Element Documentation
          Include Rung/Address Annotation
        Options
          Append to <filename>
          Element/Nicknames (Use Element Names, Use Nicknames)
          Parameter Delimiters (Use Spaces, Use Tabs)

## Slide 6: Project Management
Project Saving
  File 
    Export 
      Generate DMLoader Image… - creates image file for DMLoader
        DMLoader Image Password
        Comm Session Password [if PLC has password]
        $ProductID – $ProductID (DST387) useful for ensuring the image is authorized for the target PLC (8-digit hex value)
        $ProductVersion - $ProductVersion (DST388), 8-digit hex: MMmmBBBB (MM: Major, mm: minor, BBBB: build)
        PLC Operating System – update OS
        Program, System Configuration and Documentation
        Retentive Memory Image
        Password Configuration
        User Provided Banner Bitmap
        User Provided Instruction File

## Slide 7: Project Management
Project Saving
  File 
    Export 
      Element Documentation…- Creates text-only version of element documentation. Designed for backup.
        Standard Format: Element, Nickname, Extra Info, Description
        Standard Format PLUS export multi-line description as multiple CSV fields
        C-more™ Format: Tag Name (Nickname), Value Type, Element, Block Type, Block Name
        C-more™ Format PLUS All Used Elements

## Slide 8: Project Management
Project Saving
  File 
    Export 
      Memory Data…
Allows a user-defined list of memory elements to be saved into a CSV (comma-separated variable) file.

## Slide 9: Project Management
Project Saving
  Tools 
    Memory Image Manager…
      Snapshots retentive memory: “Generate New Image” button
      Saves in project
      Save only what you want
      “Enable Automatic Download” – when writing to the PLC

## Slide 10: Project Management
Project Storage
  File 
    Manage Projects 
      Folder Settings…
        Projects Folder – location of all project files
        Backup Folder – location of Backup files (File  Backup Project)
          <Set Backup Folder to Default>
        Auto Save Folder – location of AutoSave files
          <Set the Number to Keep> button
        Edit History Folder – locations of files created by Restore Point process (Edit  Edit History…)

## Slide 11: Project Management
Project Creation
  File 
    New Project 
      Offline…
      Online…

## Slide 12: Project Management
Project Editing
  File 
    Open Project…
    Read Project from PLC
    Import 
      Project…
      Element Documentation…
        Merge (Project priority)
        Merge (.CSV File priority)
        Delete existing
      Memory Data… (following slides)
      Migrate DirectSOFT Project… (following slides)

## Slide 13: Project Management
Project Editing
  File 
    Import 
      Memory Data…
        Follow the rules
Bit / Numeric:
  Delimited by comma
  Valid data for type
  Start bits on byte boundary
Text:
  Enclose in “”
  Observe escape sequence for special characters (e.g. $)
CSV File

## Slide 14: Project Management
Project Editing
  File 
    Import 
      Migrate DirectSOFT Project…

## Slide 15: Project Management
Project Editing
  Tools 
    Insert Instructions From File… (text file)
      Instruction Import Method
        As Code Blocks: imported as new code blocks in project
        As Rungs of Logic: imported as logic in existing code block
          Import Rungs into Code Block: choose code block
          Insert at Beginning / End / Before Rung Number
      Documentation Import Method
        Merge (.DMD Priority)
        Merge (.TXT Priority)
        Ignore Element Documentation: retains current documentation
      Ignore MEM_CONFIG Sections: Disables memory configuration (Heap Items & Memory Blocks that may be required by instructions being imported)