## Slide 1: Do-more Technical Training
System Security

## Slide 2: System Security
Hardware Security
  Mode Switch in RUN or STOP provides a minimal protection against software-commanded PLC mode change
  Dipswitch #3 offers the ability to disable firmware/gate array updates

## Slide 3: System Security
Multiple User Accounts
Session-based Communication
Protocol-specific Memory
Code-Block Protection
Sessions Locked Out

## Slide 4: System Security
Multiple User Accounts
  Do-more CPU has “Default User” predefined
    Password is blank (cannot be changed)
    Has all privileges
    Privileges can only be modified after adding an Admin & logging in as Admin
  First user created must be Administrator
  Can add up to 16 users
  Each account can have different levels of access
    RD – Read Data SS – System Settings
    WD – Write Data PM – Change PLC Mode
    RP – Read Project PW – Change Password
    WP – Write Project FW – Update Firmware
  Minimum privileges are RD (Read Data) & RP (Read Project)

## Slide 5: System Security
Multiple User Accounts
  Privileges
    *RD (Read Data) – allows reading of all data locations
    WD (Write Data) – allows writing of all data locations
    *RP (Read Project) – allows reading of the ladder program, system configuration & documentation from the PLC
    WP (Write Project) – allows writing of the ladder program, system configuration & documentation to the PLC
    SS (System Settings) – allows setting of system clock, clearing system & user logs
    PM (Change PLC Mode) – allows changing of PLC mode (Program/Run) & invoking of debug features
    PW (Change Password) – allows management of user accounts; without this privilege the Password Configuration cannot be opened
    FW (Update Firmware) – allows updating of PLC’s firmware
  *Minimum privilege

## Slide 6: System Security
Multiple User Accounts
  3 Ways to Clear the Password Configuration
    (1) Use Password Configuration to delete User Accounts
      Administrator can only be deleted if it is the only account
        If Administrator is deleted, Default User resets to default privileges & blank password
    (2) Clear PLC Memory with appropriate option
    (3) Manual hardware reset

## Slide 7: System Security
Session-based Communication
  Unique ID used in all communication telegrams
    If not present, PLC discards telegram
    Prevents unauthorized access to PLC
    Prevents other PCs from accessing wrong PLC
  Sessions can timeout
    If it times out, must be reestablished

## Slide 8: System Security
Protocol-specific Memory (Guest Memory)
  Prevents external devices from randomly accessing PLC’s I/O & memory
  Modbus Protocol (RTU & TCP)
    Server (Slave)
      MI – Input
      MIR – Input Register
      MC – Coil
      MHR – Holding Register
    Client (Master)
      Use MWX – Modbus Network Write instruction
      Use MRX – Modbus Network Read instruction

## Slide 9: System Security
Protocol-specific Memory (Guest Memory)
  Modbus Server (Slave)

## Slide 10: System Security
Protocol-specific Memory (Guest Memory)
  Modbus Client (Master)

## Slide 11: System Security
Protocol-specific Memory (Guest Memory)
  DL Protocol (K-sequence)
    Server (Slave)
      DLX – Input
      DLY – Output
      DLC – Bit
      DLV – V-memory
    Client (Master)
      Use DLWX – DirectLOGIC Network Write instruction
      Use DLRX – Direct LOGIC Netwrok Read instruction
  NOTE: DirectNET protocol is not supported

## Slide 12: System Security
Protocol-specific Memory (Guest Memory)
  DL Server (Slave)

## Slide 13: System Security
Protocol-specific Memory (Guest Memory)
  DL Client (Master)

## Slide 14: System Security
Code-Block Protection
  Full Access
    Viewed & modified without restriction
  Unlocked for this Project Session
    Password-protected, but can be viewed & modified until the project is closed.
  Locked
    Password-protected & can only be modified on a per-operation basis (e.g. editing the Code-Block Configuration), & then only when the correct Password is entered

## Slide 15: System Security
Sessions Locked Out
  CPU counts failed attempts to login
    8 consecutive fails:
      30-second lockout
      $LoginLockedOut (ST150) = ON
        This bit could be used in ladders to store the time (i.e. $Now (SDT0)) of the lockout
    After 30 seconds:
      Attempts can be resumed
      $LoginLockedOut (ST150) = OFF
    $FailedLoginCnt (DST386) is a running total of failed login attempts

## Slide 16: System Security
Associated Instructions
  DATAINFO (Category: Misc/Data Manipulation)
  HWINFO (Category: Hardware/Device)

## Slide 17: System Security
DATAINFO “Query Information about Data memory”
  Reads the size or Schema ID of a Data Block or Heap Item
  Parameters:
    Memory Type:
      Data Block – a list of all Data Blocks configured
      Information Type:
        Number of Elements in Block
        Number of BYTEs in Block
        Number of BITs in Block
        Data Type ID (Schema ID)
      Heap Item – a list of all Heap Items configured
      Information Type:
        Number of DWORDs in Heap Item
        Data Type ID (Schema ID)
    Output – location of read value
    Input Leg
      Edge triggered
      Power flow enabled
Schema ID | Description | Schema ID | Description
1 | BIT | 265 | File
2 | Unsigned BYTE | 266 | Program
3 | Signed BYTE | 267 | Device Reference
4 | Unsigned WORD |  | 
5 | Signed WORD | 268 | CTRIO
6 | Signed DWORD | 269 | CTRIO Counter
7 | REAL | 270 | CTRIO Timer
 |  | 271 | CTRIO Pulse Catch
256 | Timer | 272 | CTRIO Pulse
257 | Counter | 273 | CTRIO Discrete
258 | String | 274 | CTRIO Raw
259 | PID |  | 
260 | Clock | 275 | Drum
261 | Task | 276 | Stream
262 | Peerlink | 277 | Server
263 | RampSoak | 278 | Packet
264 | Reserved | 279 | Process Simulator

## Slide 18: System Security
HWINFO “Get Hardware Information”
  Reads hardware-specific info from I/O module
  Parameters:
    Information Type:
      Module ID – see Help File for all IDs (there’s a bunch!)
      X Count
      Y Count
      WX Count
      WY Count
      DX Count
      DY Count
    Master:
      LocalIOMaster – local I/O base
      EthIOMaster – Ethernet I/O remote base
    Base
    Slot
    Output – location for read value