## Slide 1: Do-more Technical Training
Do-more Designer Simulator

## Slide 2: Simulator
Virtual PLC
  PLC  Launch Do-more Simulator
  Uses same control engine as a Do-more PLC
  Components
    CPU
      Uses PC’s NIC
      Can use PC’s COM port
        Sim  Select Comm Port
    16-point discrete input module
    16-point discrete output module
    8-channel analog input module
    8-channel analog output module
  Shows some key memory areas

## Slide 3: Simulator
Virtual PLC
  Do-more Designer talks to the SIM like it would a real Do-more CPU
    Link is preconfigured to talk over 127.0.0.1; the PC’s NIC
  System Configuration & Memory Configuration can be changed
  I/O Configuration is fixed
  Projects are downloaded just like real CPU
  If in RUN mode, executed ladder logic
    Only says in RUN mode for 1 hour

## Slide 4: Simulator
Virtual PLC
  Discrete inputs (X0-X15)
    Toggles OFF/ON on click
    Disable: Sim  Enable Inputs
  Discrete outputs (Y0-Y15)
    Indicates OFF/ON
  Analog inputs (WX0-WX7)
    Click & drag slider bars
  Analog outputs (WY0-WY7)
    Bar indicates value
  Memory status
    Similar to a Data View
  Pressing <Exit> button is the same as turning OFF your PLC
    Do-more Designer will get a Link Error (disconnect)

## Slide 5: Simulator
Virtual PLC
  SIM has PID Process Simulator built in
  Sim  Setup PID Process Simulator
  Uses 1st-order filter plus a dead-time calculation
  I/O used:
    WX0 as Process Variable (PV)
    WX1 as Set Point (SP)
    WY0 as Output (Output)
  PID Process Simulator structure ($IntProcSim)
    DeadTime
    TimeConstant
    Noise
    Enable
  Pressing <What else do I need to do?> button   

## Slide 6: Simulator
Virtual PLC
  PID instruction required
  SCALE instruction required
  Follow instructions