## Slide 1: Do-more Technical Training
System Configuration
(I/O Mapping)

## Slide 2: System Configuration
I/O Mapping
  Grouped by I/O Master
  Then by Base/Slave
  Headings:
    Slot
    Mod ID
    Mod Description
    Slot I/O
    X Map / Y Map / WX Map / WY Map
Notes: Launchpad: nothing new here
Project Browser:
  Buttons
    Control Logic Filter – Display filter
    New Code Block – Create new code blocks
    Execution Order – Change execution order of blocks
    Status – Shows which blocks are enabled to run
    Sort Code Blocks – Change display order
    Sort Memory – Change display order
  Control Logic
  Configuration
  Tools
Debug View
  NOTE: Message Dump – enables dump to Do-more Logger, $EnableMsgDump (ST36)
Data View
PID Overview

## Slide 3: System Configuration
I/O Mapping
  Decimal Addressing!
  Auto – addresses are gray
    PLC assigns addresses
  Manual – addresses are black
    User-assigned addresses
      Only beginning address can be specified
  Map range overlaps are red
  Map values exceeding memory range are bold red
  Right-click to edit base’s default map
  Clear Manual Entries
WARNING
Manual configuration can change the mapping for other modules!
Notes: Launchpad: nothing new here
Project Browser:
  Buttons
    Control Logic Filter – Display filter
    New Code Block – Create new code blocks
    Execution Order – Change execution order of blocks
    Status – Shows which blocks are enabled to run
    Sort Code Blocks – Change display order
    Sort Memory – Change display order
  Control Logic
  Configuration
  Tools
Debug View
  NOTE: Message Dump – enables dump to Do-more Logger, $EnableMsgDump (ST36)
Data View
PID Overview